## Slide 1
SDSCPA
DESIGN & PRODUCTION
Theatre Safety
Classroom Lab
Grade 10 → Grade 9 → Grade 8
Teach the rules. Ask the room. Reveal the answer. Certify safe practice.
100%
REQUIRED
SDSCPA · SAFETY LAB · CLASSROOM DECK
1
Notes: Open by establishing the standard: safety certification requires complete understanding, instructor permission, and hands-on qualification.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 2
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · HOW TO USE THIS DECK
2
Pause before every reveal
The question slide always comes first. Advance only after students commit to an answer.
1
ASK
Read the prompt aloud and give students quiet think time.
2
COMMIT
Take a hand vote, cold-call, or ask partners to agree on one response.
3
REVEAL
Advance one slide. Compare the answer with the class reasoning.
4
TRANSFER
Connect the rule to the actual shop, tool, or rehearsal situation.
Notes: Use the deck as a discussion tool, not a passive lecture. The answer slide is deliberately separate so students must reason before seeing the correction.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 3
THEATRE SAFETY CERTIFICATION
GRADE 10
Independent-use qualification begins with disciplined judgment.
13 MODULES · 85 TRAINING SECTIONS · 24 CLASSROOM CHECKS
SDSCPA · SAFETY LAB · GRADE 10
3
Notes: Introduce the Grade 10 section and name the level of supervision students are working toward.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 4
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 01 OF 13
4
MODULE 01
Shop Safety & PPE
Dress code, hazards, PPE, lifting, housekeeping, emergencies, and safety culture.
Welcome to certification week: This week you earn your shop certification - proof that you know every rule and every tool you’re responsible for at your grade level, including…
Dress for the shop: Shop safety starts before you touch a tool - with what you’re wearing: Closed-toe shoes, every shop day.
Emergencies & injuries: Know these before you touch a single tool: If anyone yells “STOP” or “HOLD” , all work stops instantly - no questions, hands off, tools down.
Dust - the slow hazard: The hazard you can’t feel hurting you: Fine wood dust harms lungs over years , not minutes - which is why nobody takes it seriously until it’s late.
Model safe work - independently: At your level, safety isn’t something done to you - it’s something you model .
13 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Welcome to certification week
This week you earn your shop certification - proof that you know every rule and every tool you’re responsible for at your grade level, including everything from past years.
Plan on about 45 minutes of training a day : Days 1–4 are training modules, Day 5 is the certification quiz. The quiz needs 100% - and anything you miss sends you back to retrain that module. That’s not punishment; it’s how real shops qualify people.
Passing this lab is step one of the district’s safety program. Before you operate anything, your teacher still gives you hands-on demonstrations and a guided-practice sign-off on each piece of equipment - and nothing in this shop is ever operated without the instructor’s permission .
Permission & attention
The rule the district prints in capital letters: DO NOT OPERATE EQUIPMENT WITHOUT PERMISSION FROM THE INSTRUCTOR. Not before class, not during, not after - safety instruction and the instructor’s go-ahead come first, every time.
Keep your mind on the work. A moment of lost attention is how serious accidents happen.
No earbuds or headphones in the work environment - they mask warnings, callouts, and the sound of a machine going wrong. (Production intercom during shows is the one exception, used with discipline.)
When in doubt, ask the instructor - not the student next to you.
Dress for the shop
Shop safety starts before you touch a tool - with what you’re wearing:
Closed-toe shoes, every shop day. No sandals, no slides, no exceptions - dropped lumber doesn’t care how careful you were.
Long hair tied back. Hair near a spinning tool gets pulled in faster than you can react.
No dangling anything - jewelry, hoodie strings, loose sleeves, lanyards. If it hangs, it catches.
Sleeves rolled above the elbows , nothing loose at the wrists.
Gloves only where the task calls for them - rough lumber, hot fixtures, chemicals. Never around spinning blades or bits: a caught glove pulls the hand in with it.
No running, no horseplay. Ever. The shop is the one room where a joke shove can cost a finger.
Know your hazards
A theatre shop is full of things that can hurt you if you don’t see them coming: sharp tools and blades , things falling from above , dust in the air , loud noise , and cords, lumber, and clutter you can trip over .
Your first safety skill is simple: look around and name the hazards before you start any task. If you can’t name what could go wrong, you’re not ready to start.
Spot the hazards
Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Lifting & carrying
More shop injuries come from carrying than from cutting:
Lift with your legs - squat, keep your back near-vertical, hug the load close, stand. Your back is not a crane.
Never lift more than you can handle easily - over about 25 pounds, get help.
Clear your path before you pick anything up - most carrying accidents are collisions with things left on the floor or hanging at head height.
Team-lift anything long or heavy , and lift on a call: “ready - lift on three.” Same for setting down.
Carrying long stock: watch both ends , keep the front end high, and call the corners (“coming around!”).
Gloves for rough lumber - splinters are the tax on bare hands.
Watch the pinch points when setting anything down: fingers out from under, always.
Emergencies & injuries
Know these before you touch a single tool:
If anyone yells “STOP” or “HOLD” , all work stops instantly - no questions, hands off, tools down.
Every injury gets reported to the teacher immediately - no matter how slight - and an incident report is filed. A tiny cut in a dusty shop gets infected; a “small” incident often means a hazard that will hurt the next person worse.
Know where the first-aid kit lives.
Fire gets its own full module - alarms, exits, extinguisher classes, and how to report one.
PPE without reminders
You’ve been introduced to PPE - now the bar is higher: select and wear the correct PPE for the task without being reminded .
Safety glasses for cutting and drilling, hearing protection around loud tools, dust protection when sanding. Nobody should ever have to tell you. If you’re reaching for a tool, you’ve already reached for your PPE.
Pre-use check: good to go, or report it?
Before using any tool you do a pre-use safety check - and anything unsafe gets reported , even if it isn’t yours. Sort each finding:
Dust - the slow hazard
The hazard you can’t feel hurting you:
Fine wood dust harms lungs over years , not minutes - which is why nobody takes it seriously until it’s late. Take it seriously now.
Dust collection on whenever the sander or saws run.
Clean up dust by sweeping or vacuuming - never by blasting it airborne with the compressor.
The dust mask is for making dust and for cleaning it up .
Chemicals, SDS & the eyewash station
Paint, adhesives, solvents, and fog fluid are chemicals - and every chemical in the shop has a Safety Data Sheet (SDS) :
The SDS binder lists each product’s hazards, handling rules, and first aid. Know where it lives.
Chemicals stay in labeled, closed containers - never in mystery cups or water bottles.
Rubber gloves are the exception to the no-gloves rule: wear them for stains, resins, and bleaches (never around spinning machines).
Know where the eyewash station is before you need it - you won’t be able to look for it with chemicals in your eyes.
Model safe work - independently
At your level, safety isn’t something done to you - it’s something you model . You’re expected to work safely without supervision , hold all your tool safety qualifications , and anticipate hazards before they occur instead of reacting after.
Ask yourself before every task: what’s the most likely way this goes wrong, and what am I doing about it right now?
You are the safety culture
Younger students learn shop safety mostly by watching you - and never let “we’re in a hurry” beat “we do it safely.”
A younger student picks up the impact driver without safety glasses on. The teacher is across the shop. What does the shop expect of you?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 5
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
5
ASK THE ROOM
Spot the hazards
Shop Safety & PPE
Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Which items are hazards?
• Extension cord run across the walkway
• Hand saw left blade-up on the bench
• Boxes stacked in front of the exit
• Open drink next to the work area
• Board with a nail sticking out
• Safety glasses on the PPE shelf
• Fire extinguisher on its wall hook
• Swept floor, broom racked
Notes: Ask students to commit before advancing.
Prompt: Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Extension cord run across the walkway: Trip hazard - cords get routed out of walking paths.
Hand saw left blade-up on the bench: Sharp edges get sheathed or racked, never left out.
Boxes stacked in front of the exit: Exits stay clear - always.
Open drink next to the work area: Spills around tools and electricity - drinks stay out of the shop.
Board with a nail sticking out: Pull or bend nails the moment you see them.
Safety glasses on the PPE shelf: that’s exactly where PPE belongs.
Fire extinguisher on its wall hook: visible and ready - just right.
Swept floor, broom racked: good housekeeping is what prevents hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 6
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
6
REVEAL
Spot the hazards
Shop Safety & PPE
HAZARDS
• Extension cord run across the walkway
• Hand saw left blade-up on the bench
• Boxes stacked in front of the exit
• Open drink next to the work area
• Board with a nail sticking out
SAFE / CORRECT
• Safety glasses on the PPE shelf
• Fire extinguisher on its wall hook
• Swept floor, broom racked
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Extension cord run across the walkway: Trip hazard - cords get routed out of walking paths.
Hand saw left blade-up on the bench: Sharp edges get sheathed or racked, never left out.
Boxes stacked in front of the exit: Exits stay clear - always.
Open drink next to the work area: Spills around tools and electricity - drinks stay out of the shop.
Board with a nail sticking out: Pull or bend nails the moment you see them.
Safety glasses on the PPE shelf: that’s exactly where PPE belongs.
Fire extinguisher on its wall hook: visible and ready - just right.
Swept floor, broom racked: good housekeeping is what prevents hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 7
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
7
ASK THE ROOM
Pre-use check: good to go, or report it?
Shop Safety & PPE
Before using any tool you do a pre-use safety check - and anything unsafe gets reported , even if it isn’t yours. Sort each finding:
Sort each item into: Good to go / Report it
• Guard snaps back over the blade smoothly
• Cord jacket is cracked near the plug
• Blade is burning the wood and cutting slowly
• Work area clear, stock supported on both sides
• Someone left a puddle of paint by the bench
Notes: Ask students to commit before advancing.
Prompt: Before using any tool you do a pre-use safety check - and anything unsafe gets reported , even if it isn’t yours. Sort each finding:
Guard snaps back over the blade smoothly: That’s what a working guard looks like.
Cord jacket is cracked near the plug: Damaged cords come out of service before they bite someone.
Blade is burning the wood and cutting slowly: That’s a dull blade - and a dull blade is an unsafe blade.
Work area clear, stock supported on both sides: That’s a pre-use check passing.
Someone left a puddle of paint by the bench: Unsafe conditions get reported even when they aren’t yours.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 8
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
8
REVEAL
Pre-use check: good to go, or report it?
Shop Safety & PPE
Good to go
• Guard snaps back over the blade smoothly
• Work area clear, stock supported on both sides
Report it
• Cord jacket is cracked near the plug
• Blade is burning the wood and cutting slowly
• Someone left a puddle of paint by the bench
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Guard snaps back over the blade smoothly: That’s what a working guard looks like.
Cord jacket is cracked near the plug: Damaged cords come out of service before they bite someone.
Blade is burning the wood and cutting slowly: That’s a dull blade - and a dull blade is an unsafe blade.
Work area clear, stock supported on both sides: That’s a pre-use check passing.
Someone left a puddle of paint by the bench: Unsafe conditions get reported even when they aren’t yours.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 9
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 02 OF 13
9
MODULE 02
Fire Safety & Emergencies
Alarms, exits, extinguisher classes, reporting a fire, and flammable storage.
Alarms, drills & exits: Fire safety starts before there’s ever a fire: Know the fire bell/alarm and the fire-drill procedure for the shop and the theatre.
Reporting a fire: If you discover a fire: Immediately notify the closest adult with the exact location and the nature of the fire (what’s burning).
Fire classes & extinguishers: Extinguishers match the fire - the wrong one can make it worse: Class A - wood, paper, cloth.
Flammables, rags & finishes: The scene shop makes its own fire hazards: Rags soaked with finish, stain, or solvent go in a covered metal container - oily rags in a pile can…
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Alarms, drills & exits
Fire safety starts before there’s ever a fire:
Know the fire bell/alarm and the fire-drill procedure for the shop and the theatre.
Know every fire-exit location - and keep all exits and corridors clear at all times . In an evacuation, a blocked hallway costs lives, not minutes.
Know the types and locations of the fire extinguishers in your space - before you need them.
Reporting a fire
If you discover a fire:
Immediately notify the closest adult with the exact location and the nature of the fire (what’s burning).
Do NOT shout “Fire!” - panic in a crowded theatre is its own disaster; information moves faster than fear.
If someone’s clothing catches fire: smother the flames - get them down and roll them in a blanket if one is close.
Fire classes & extinguishers
Extinguishers match the fire - the wrong one can make it worse:
Class A - wood, paper, cloth. Water or CO₂ works.
Class B - flammable liquids (paint thinner, solvents). Smother it : foam or CO₂. Water spreads it.
Class C - electrical equipment. Non-conducting only : CO₂ or dry powder. Never water - electricity travels up the stream to you.
Pick the extinguisher
Match the fire to the response:
You spot smoke
You smell smoke and find a small fire behind the scene shop. What do you do first?
Flammables, rags & finishes
The scene shop makes its own fire hazards:
Rags soaked with finish, stain, or solvent go in a covered metal container - oily rags in a pile can self-ignite . That’s not a myth; it’s chemistry.
Use finishes and solvents only in well-ventilated areas, away from open flame and heat.
Keep flammable items away from lighting instruments - and instruments away from soft goods, paper, and scenery that could cook against a hot fixture.
Pyrotechnics, flame effects, and prop firearms are never student-operated - district approval and the fire marshal come first, every time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 10
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
10
ASK THE ROOM
Pick the extinguisher
Fire Safety & Emergencies
Match the fire to the response:
Sort each item into: Water works (Class A) / CO₂ / dry powder only
• Scrap lumber and paper burning in the bin
• A dimmer rack sparking and smoking
• Spilled paint thinner catches fire
• Muslin scraps smoldering in the paint corner
Notes: Ask students to commit before advancing.
Prompt: Match the fire to the response:
Scrap lumber and paper burning in the bin: Class A - ordinary combustibles; water or CO₂.
A dimmer rack sparking and smoking: Class C electrical - non-conducting extinguisher, never water.
Spilled paint thinner catches fire: Class B flammable liquid - smother with foam or CO₂; water spreads it.
Muslin scraps smoldering in the paint corner: Class A - cloth burns like paper.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 11
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
11
REVEAL
Pick the extinguisher
Fire Safety & Emergencies
Water works (Class A)
• Scrap lumber and paper burning in the bin
• Muslin scraps smoldering in the paint corner
CO₂ / dry powder only
• A dimmer rack sparking and smoking
• Spilled paint thinner catches fire
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Scrap lumber and paper burning in the bin: Class A - ordinary combustibles; water or CO₂.
A dimmer rack sparking and smoking: Class C electrical - non-conducting extinguisher, never water.
Spilled paint thinner catches fire: Class B flammable liquid - smother with foam or CO₂; water spreads it.
Muslin scraps smoldering in the paint corner: Class A - cloth burns like paper.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 12
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
12
ASK THE ROOM
You spot smoke
Fire Safety & Emergencies
You smell smoke and find a small fire behind the scene shop. What do you do first?
Choose the safest response.
• A. Shout “Fire!” so everyone hears
• B. Notify the closest adult with the exact location and what’s burning
• C. Find a bucket of water
• D. Investigate how it started
Notes: Ask students to commit before advancing.
Prompt: You smell smoke and find a small fire behind the scene shop. What do you do first?
Exact location and the nature of the fire, to the nearest adult, immediately - and never a panic shout.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 13
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
13
REVEAL
You spot smoke
Fire Safety & Emergencies
CORRECT ANSWER
• Notify the closest adult with the exact location and what’s burning
WHY IT MATTERS
Exact location and the nature of the fire, to the nearest adult, immediately - and never a panic shout.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Exact location and the nature of the fire, to the nearest adult, immediately - and never a panic shout.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 14
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 03 OF 13
14
MODULE 03
Your Tools This Year
What’s new for you this year - and everything you carry forward.
Grade 10 - Tech 3-4: All Grade 8-9 hand and power/pneumatic tools move to independent-use level (after qualification), and you add: Stationary machines (safety orientation…
2 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Grade 10 - Tech 3-4
All Grade 8-9 hand and power/pneumatic tools move to independent-use level (after qualification), and you add:
Stationary machines (safety orientation required) - table saw, palm router, band saw .
Rigging - Nicopress swaging tool & wire-rope cutters.
Props - 3D printer, vacuum former, casting & molding equipment.
Painting - snap line, lining sticks, stencils.
Qualified - or new this year?
Sort your tools: which do you qualify to use independently , and which are new and need a fresh safety orientation with direct supervision?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 15
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
15
ASK THE ROOM
Qualified - or new this year?
Your Tools This Year
Sort your tools: which do you qualify to use independently , and which are new and need a fresh safety orientation with direct supervision?
Sort each item into: Independent (after qualification) / New - orientation first
• Jigsaw
• Impact driver
• Framing nailer
• Table saw
• Palm router
• Band saw
Notes: Ask students to commit before advancing.
Prompt: Sort your tools: which do you qualify to use independently , and which are new and need a fresh safety orientation with direct supervision?
Jigsaw: A Grade 8-9 tool - pass the independent-use qualification and it’s yours.
Impact driver: A Grade 8-9 tool - pass the independent-use qualification and it’s yours.
Framing nailer: A Grade 8-9 tool - pass the independent-use qualification and it’s yours.
Table saw: New this year - safety orientation, then direct supervision at first.
Palm router: New this year - safety orientation, then direct supervision at first.
Band saw: New this year - safety orientation, then direct supervision at first.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 16
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
16
REVEAL
Qualified - or new this year?
Your Tools This Year
Independent (after qualification)
• Jigsaw
• Impact driver
• Framing nailer
New - orientation first
• Table saw
• Palm router
• Band saw
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Jigsaw: A Grade 8-9 tool - pass the independent-use qualification and it’s yours.
Impact driver: A Grade 8-9 tool - pass the independent-use qualification and it’s yours.
Framing nailer: A Grade 8-9 tool - pass the independent-use qualification and it’s yours.
Table saw: New this year - safety orientation, then direct supervision at first.
Palm router: New this year - safety orientation, then direct supervision at first.
Band saw: New this year - safety orientation, then direct supervision at first.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 17
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 04 OF 13
17
MODULE 04
Hand Tools & Knives
Tape measure, utility knife, squares, hammer, screwdrivers, hand saw - the tools everything else is built on.
Measuring & layout tools: Even “safe” tools have rules: Tape measure - control the blade on the way back in; a spring-loaded steel edge returning at full speed can cut.
Utility knife: The tool you’ll use most, and the one that sends the most people to the first-aid kit: • A sharp blade is safer than a dull one - it needs less force, so…
Hammer, screwdrivers & hand saw: Hammer - check the head is tight before swinging; clear your swing arc (people and your other hand); start nails with a light tap, fingers gone before…
3 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Measuring & layout tools
Even “safe” tools have rules:
Tape measure - control the blade on the way back in; a spring-loaded steel edge returning at full speed can cut. Watch the hook edge on long pulls.
Marking & layout tools - carry pointed tools (awls, compasses, pencils) tip-down , and never walk with them in a pocket point-up.
Every tool goes back to its rack when you set it down - a bench you can’t see the surface of is a bench hiding a blade.
Utility knife
The tool you’ll use most, and the one that sends the most people to the first-aid kit:
• A sharp blade is safer than a dull one - it needs less force, so it slips less. Swap dull blades.
• Cut away from your body - and away from the hand bracing the work. Ask: “if this slips, where does the blade finish?”
• Cut on a mat or scrap , never on the bare table or your knee.
• Retract the blade the second you stop cutting. No exceptions.
• Pass it handle-first , blade retracted. Used snap-off blades go in the taped sharps container, never loose in the trash.
Hammer, screwdrivers & hand saw
Hammer - check the head is tight before swinging; clear your swing arc (people and your other hand); start nails with a light tap, fingers gone before the real swing.
Screwdrivers - use the right size tip so it doesn’t cam out; never drive toward your palm or hold the work in your hand; a screwdriver is not a chisel or a pry bar - tips snap and hands slip.
Hand saw - start the kerf with short, light strokes; keep your free hand clear of the cut line; support the off-cut so it doesn’t tear free at the end.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 18
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 05 OF 13
18
MODULE 05
Costume & Craft Tools
Needles, pins, shears, papier-mâché & armatures, the sewing machine, and the hot-wire foam knife.
Needles, pins & hand sewing: Small tools, real rules: Count your needles and pins out - and back in.
Scissors & pattern tools: Fabric shears are seriously sharp - that’s the point.
Papier-mâché & armatures: Props building has its own sharp ends: Cut armature wire with wire cutters, never scissors - scissors get ruined, and ruined tools slip.
Sewing machine: The machine drives a needle up and down faster than you can react - respect the zone around it: • Fingers stay a needle-width away - guide fabric from…
Hot-wire foam knife: It doesn’t look dangerous - it’s a wire.
8 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Needles, pins & hand sewing
Small tools, real rules:
Count your needles and pins out - and back in. A lost pin ends up in a costume, a couch, or a foot.
Pins live in a pincushion or magnetic tray - never in your lips, never in your clothes.
Broken needles and bent pins get taped and binned , not tossed loose.
Anything sharp gets passed handle-first .
Scissors & pattern tools
Fabric shears are seriously sharp - that’s the point.
• Carry them closed, point-down . Never run - it’s a cliché because it’s true.
• Pass them handle-first .
• Cut on the table , fabric flat, free hand behind the blades - not in the air toward yourself.
• Fabric shears cut fabric only : paper and cardboard dull them into tools that slip.
Papier-mâché & armatures
Props building has its own sharp ends:
Cut armature wire with wire cutters, never scissors - scissors get ruined, and ruined tools slip.
Every cut wire end gets bent back or taped immediately. Armature wires stick out at exactly eye height on a crowded work table.
Paste makes floors slick - wipe drips when they happen, not at cleanup.
Cover cuts on your hands before pasting, and wash up after - paste and sealers aren’t hand lotion.
Wire ends
You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Sewing machine
The machine drives a needle up and down faster than you can react - respect the zone around it:
• Fingers stay a needle-width away - guide fabric from the sides, never push it from directly in front of the needle.
• No loose sleeves, jewelry, or hair near the needle and handwheel.
• Control speed with the pedal - start slow ; speed is earned, not assumed.
• Power off (or unplug) before changing the needle or working close to it.
• Let the machine stop completely before reaching in to pull threads or fabric.
Sewing machine check
The needle on your machine is bent and needs changing. First move?
Hot-wire foam knife
It doesn’t look dangerous - it’s a wire. But it cuts by heat :
The wire burns skin instantly and stays hot after you switch it off - it rests on its stand until cool.
Only cut approved foam (polystyrene). Unknown foams and polyurethane can release toxic fumes when hot. If you don’t know what the foam is, you don’t cut it.
Cut with ventilation on , away from anything flammable.
A burn gets cool water and gets reported - like every injury.
Hot-wire check
A scrap of foam with no label shows up in the bin, and it would be perfect for your prop. Hot-wire it?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 19
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
19
ASK THE ROOM
Wire ends
Costume & Craft Tools
You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Choose the safest response.
• A. Finish the layer first, then deal with it
• B. Bend it back or tape it immediately
• C. Point it out to the people nearby
• D. Move your own face away from it
Notes: Ask students to commit before advancing.
Prompt: You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 20
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
20
REVEAL
Wire ends
Costume & Craft Tools
CORRECT ANSWER
• Bend it back or tape it immediately
WHY IT MATTERS
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 21
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
21
ASK THE ROOM
Sewing machine check
Costume & Craft Tools
The needle on your machine is bent and needs changing. First move?
Choose the safest response.
• A. Change it quickly while the machine idles
• B. Power off or unplug the machine before touching the needle
• C. Turn the handwheel with your finger near the needle to check it first
• D. Speed the pedal to snap the needle out
Notes: Ask students to commit before advancing.
Prompt: The needle on your machine is bent and needs changing. First move?
A pedal bump with your fingers at the needle is exactly how sewing-machine injuries happen - kill the power first.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 22
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
22
REVEAL
Sewing machine check
Costume & Craft Tools
CORRECT ANSWER
• Power off or unplug the machine before touching the needle
WHY IT MATTERS
A pedal bump with your fingers at the needle is exactly how sewing-machine injuries happen - kill the power first.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
A pedal bump with your fingers at the needle is exactly how sewing-machine injuries happen - kill the power first.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 23
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 06 OF 13
23
MODULE 06
Power Tool Basics
The rules that cover every power and pneumatic tool, and your path to qualification.
Rules that never change: For every power and pneumatic tool, at every grade level: • Guards stay on and working.
Your path: orientation → supervision → independence: Qualification is a ladder, and every tool has its own rung: 1⃣ Safety orientation (Grade 8) - you pass an orientation for each tool, then perform…
Cords, hoses & your workspace: The cable end of tool safety: The cord or hose stays behind the tool, never in the cut path - check before every cut, not after.
Clamp it, support it: Most “tool accidents” are really workholding accidents : A clamp beats your strongest grip - and it never flinches.
Pneumatic power: the air rules: The stapler and nailer run on compressed air, which adds rules of their own: • Treat every air tool as loaded.
7 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Rules that never change
For every power and pneumatic tool, at every grade level:
• Guards stay on and working. A tool with a faulty guard doesn’t get used - it gets reported.
• PPE first - safety glasses always; hearing and dust protection as the task demands.
• Correct body position - balanced stance, hands clear of the cut line, never reaching across a blade.
• Disconnect power or air before adjusting - blade changes, depth settings, or clearing jams happen only on a dead tool.
Your path: orientation → supervision → independence
Qualification is a ladder, and every tool has its own rung:
1⃣ Safety orientation (Grade 8) - you pass an orientation for each tool, then perform fundamental operations under direct supervision : straight cuts, crosscuts, driving fasteners, sanding flat stock.
2⃣ General supervision (Grade 9) - you set up and operate each tool with the teacher in the shop, not at your elbow, producing accurate cuts and secure assemblies.
3⃣ Independent qualification (Grade 10+) - you pass an independent-use qualification per tool, handle routine adjustments yourself, and help train peers.
Grade level alone never qualifies you - passing the orientation or qualification for that specific tool does .
Notice and report
From Grade 9 on, noticing problems is part of your qualification :
• A blade that burns the wood or cuts slowly is dull - stop and report it.
• A pneumatic tool that sputters or double-fires may have low or wrong air pressure - stop and report it.
• Anything loose, cracked, wobbling, or smelling hot - stop and report it .
You are not “bothering the teacher.” You are doing the job.
Cords, hoses & your workspace
The cable end of tool safety:
The cord or hose stays behind the tool, never in the cut path - check before every cut, not after.
Never carry a tool by its cord , and unplug by gripping the plug , not yanking the cable.
Disconnecting an air hose: shut off the air and bleed the pressure first , and keep hold of the coupling - a charged hose whips.
Cords and hoses route along walls and out of walkways , same as the shop rule you already know.
Clamp it, support it
Most “tool accidents” are really workholding accidents :
A clamp beats your strongest grip - and it never flinches.
Long stock gets outfeed support - a sawhorse, a stand, or a partner on a callout.
The cut line hangs clear of the bench - cutting into the table pinches the blade and ruins both.
Never cut work resting on your knee or held in the air.
Know what’s under and behind the cut before you start it.
Pneumatic power: the air rules
The stapler and nailer run on compressed air, which adds rules of their own:
• Treat every air tool as loaded. Finger off the trigger until the nose is on the work.
• Never point one at anyone - including yourself. Ever. Even “empty.”
• Disconnect the air line before clearing a jam, adjusting, or handing it over.
• Use the tool’s correct air pressure - too high blows fasteners through the work; too low jams and double-fires.
• Hoses get routed out of walkways , like every cord.
Blade change - in order
You’re qualified for routine adjustments now. Put a safe blade change in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 24
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
24
ASK THE ROOM
Blade change - in order
Power Tool Basics
You’re qualified for routine adjustments now. Put a safe blade change in order. Tap the first step, then the next…
Put the steps in the safest order.
• Make a test cut on scrap
• Reconnect the power
• Check the blade is tight and the guard moves freely
• Swap in the new blade
• Disconnect the power
Notes: Ask students to commit before advancing.
Prompt: You’re qualified for routine adjustments now. Put a safe blade change in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 25
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
25
REVEAL
Blade change - in order
Power Tool Basics
CORRECT ORDER
• 1. Disconnect the power
• 2. Swap in the new blade
• 3. Check the blade is tight and the guard moves freely
• 4. Reconnect the power
• 5. Make a test cut on scrap
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 26
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 07 OF 13
26
MODULE 07
Power Saws: Jigsaw, Miter, Panel
Tool-by-tool specifics for the three saws you qualified on in Stagecraft.
Jigsaw: The curve-cutter.
Jigsaw - blades, curves & cutouts: Getting the cut you want, safely: Match the blade to the material - wood, metal, and scroll blades are different animals; the wrong one burns, wanders,…
Compound miter saw: The crosscut machine.
Miter saw - angles & short stock: The setups that catch people: Set and lock the angle , then test on scrap - an unlocked table creeps mid-cut.
Panel saw: The sheet-goods saw.
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Jigsaw
The curve-cutter. Its specifics:
• Clamp your stock - small pieces walk with the blade and take fingers along.
• Base plate flat on the work before you pull the trigger.
• Know what’s under the cut - the blade sticks out below the stock. Nothing under the line: not the bench edge, not the cord, not your hand.
• Let the blade stop before lifting the saw out of the cut.
• Forcing the cut bends and snaps blades - let the blade do the work . Unplug to change blades.
Jigsaw - blades, curves & cutouts
Getting the cut you want, safely:
Match the blade to the material - wood, metal, and scroll blades are different animals; the wrong one burns, wanders, and snaps.
Tight curves want narrow blades - and really tight curves want relief cuts first, so the blade never binds.
Interior cutouts start from a drilled starter hole , never from tipping the saw into the surface.
A blade that starts wandering off your line is worn out - swap it (unplugged) instead of steering harder.
Compound miter saw
The crosscut machine. Its specifics:
• Stock tight against the fence - always. A gap lets the blade grab and slam the stock.
• Hands outside the no-hand zone (at least 6 inches from the blade path). Never cross your arms - left hand holding the right side of the blade is how people meet the blade.
• Full speed before the cut - let it spin up, then bring it down smoothly.
• After the cut, keep the blade down until it stops - a spinning blade coming up can grab the off-cut and throw it.
• Support long stock on both ends; never balance it.
Miter saw - angles & short stock
The setups that catch people:
Set and lock the angle , then test on scrap - an unlocked table creeps mid-cut.
Long stock gets a stand or a partner (on a callout) at the far end - a see-sawing board pinches the blade.
Anything too short to hold outside the no-hand zone gets clamped - or cut from a longer board so your hand never gets close.
If a cut would put your fingers inside the zone, that cut doesn’t happen that way. There is always another way.
Panel saw
The sheet-goods saw. Its specifics:
• Seat the sheet fully on the rollers/rails before cutting - a cocked sheet binds the blade.
• Both hands on the carriage handle. Never steady the sheet with a hand near the cut line.
• Let the carriage return home before touching anything.
• Mind the off-cut - full sheets are heavy, and freed panels pinch fingers and toes. Get help catching big pieces.
Spot what’s wrong: the cutting station
Walk the saw stations and tap the 4 problems .
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 27
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
27
ASK THE ROOM
Spot what’s wrong: the cutting station
Power Saws: Jigsaw, Miter, Panel
Walk the saw stations and tap the 4 problems .
Which items are hazards?
• Small block held by hand for a jigsaw cut
• Fingers inside the miter saw’s no-hand zone
• Blade change with the saw still plugged in
• One hand steadying the sheet near the cut line
• Stock clamped tight to the bench
• Everyone at the station in safety glasses
• Off-cuts cleared between cuts
Notes: Ask students to commit before advancing.
Prompt: Walk the saw stations and tap the 4 problems .
Small block held by hand for a jigsaw cut: Clamp small pieces - they walk, and fingers follow.
Fingers inside the miter saw’s no-hand zone: Six inches minimum from the blade path, always.
Blade change with the saw still plugged in: Adjustments happen on dead tools only.
One hand steadying the sheet near the cut line: On the panel saw both hands stay on the carriage handle.
Stock clamped tight to the bench: exactly right - clamped stock can’t walk.
Everyone at the station in safety glasses: PPE without reminders - that’s the standard.
Off-cuts cleared between cuts: a clear station is a safe station.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 28
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
28
REVEAL
Spot what’s wrong: the cutting station
Power Saws: Jigsaw, Miter, Panel
HAZARDS
• Small block held by hand for a jigsaw cut
• Fingers inside the miter saw’s no-hand zone
• Blade change with the saw still plugged in
• One hand steadying the sheet near the cut line
SAFE / CORRECT
• Stock clamped tight to the bench
• Everyone at the station in safety glasses
• Off-cuts cleared between cuts
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Small block held by hand for a jigsaw cut: Clamp small pieces - they walk, and fingers follow.
Fingers inside the miter saw’s no-hand zone: Six inches minimum from the blade path, always.
Blade change with the saw still plugged in: Adjustments happen on dead tools only.
One hand steadying the sheet near the cut line: On the panel saw both hands stay on the carriage handle.
Stock clamped tight to the bench: exactly right - clamped stock can’t walk.
Everyone at the station in safety glasses: PPE without reminders - that’s the standard.
Off-cuts cleared between cuts: a clear station is a safe station.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 29
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 08 OF 13
29
MODULE 08
Drivers, Sanders & Nailers
Impact driver, random orbital sander, narrow crown stapler, and framing nailer.
Impact driver: Small tool, huge torque.
Bits & torque: The details that separate clean driving from stripped screws: Right bit, right size - a PH2 in a PH3 screw strips both.
Random orbital sander: The dust machine.
Grits & technique: Sanding well is sanding safely - fighting the tool is what causes slips: Work the grit ladder: 80 → 120 → 220 .
Stapler & framing nailer: You learned the air rules in Power Tool Basics - here are the gun-specific ones: • The contact safety tip on the nose is what stops accidental fires.
5 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Impact driver
Small tool, huge torque. Its specifics:
• Seat the bit fully in the screw head before pulling the trigger - a half-seated bit cams out and skates.
• Hand off the fastener line. When the bit slips, it goes exactly where your hand was going to be.
• Start slow to set the threads, then run it home.
• Brace small work - the driver will happily spin the workpiece instead of the screw.
• Eye protection: screw heads snap and bits shatter.
Bits & torque
The details that separate clean driving from stripped screws:
Right bit, right size - a PH2 in a PH3 screw strips both. Check before you drive.
Worn bits get binned , not babied - a rounded bit cams out no matter how hard you push.
Impact drivers hammer - that rattle is the mechanism working, and it’s loud : hearing protection when the driving runs long.
Small screws snap under full impact - ease off as the head seats.
Pilot holes near edges stop the split before it starts.
Random orbital sander
The dust machine. Its specifics:
• Dust protection on, dust collection attached - fine dust is the hazard you can’t see hurting you.
• Don’t press. The tool’s weight is enough; leaning on it burns the paper, scorches the stock, and stalls the pad.
• Let the pad stop before you set it down - a live sander walks off the bench.
• Secure small pieces ; the sander is strong enough to launch them.
• Keep the cord behind the tool , never under the pad.
Grits & technique
Sanding well is sanding safely - fighting the tool is what causes slips:
Work the grit ladder: 80 → 120 → 220 . Skipping grits means pressing harder for less result.
Keep the pad flat and moving - parking it in one spot digs a dish you’ll sand an hour to fix.
Edges round over in seconds - ease up when you get near them.
Let the paper do the work: if you’re pressing, the paper’s done - change it .
Stapler & framing nailer
You learned the air rules in Power Tool Basics - here are the gun-specific ones:
• The contact safety tip on the nose is what stops accidental fires. It is never held down, taped, or bypassed . Never.
• Sequential fire : nose on the work first, then the trigger.
• Hands at least a hand-span from the fire line. Staples and nails follow the grain and deflect off knots - they can exit the wood sideways .
• The framing nailer recoils - grip it, expect it.
• Carry with your finger off the trigger ; disconnect air to clear jams or hand it off.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 30
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 09 OF 13
30
MODULE 09
Stationary Machines
Table saw, band saw, and palm router - tool-by-tool specifics.
Table saw - setup: The most powerful - and least forgiving - machine in the shop.
Kickback & body position: The table saw’s biggest danger is kickback - the blade grabbing stock and throwing it back at operator speed.
Band saw: The curve machine for thick stock.
Band saw - resaw & drift: Resawing - cutting a board through its thickness into thinner boards - is a Tech 3-4 operation with its own setup: A tall fence supports the board on…
Palm router: Small base, spinning cutter, strong opinions.
9 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Table saw - setup
The most powerful - and least forgiving - machine in the shop. Each stationary machine requires its own safety orientation , then fundamental operations under direct supervision .
Setup non-negotiables:
• Blade height : teeth just clear the top of the stock - a tall blade exposes more steel for no benefit.
• Guard and riving knife in place.
• Rip fence for rips, miter gauge for crosscuts - never both together. Trapping stock between them binds the off-cut and fires it back at you.
• Push sticks and featherboards within reach before you start.
Kickback & body position
The table saw’s biggest danger is kickback - the blade grabbing stock and throwing it back at operator speed.
Defend against it: stand to the side of the blade, never directly behind the stock ; keep stock tight against the rip fence ; never cut freehand; use a push stick the moment your hand would come near the blade; and let the blade stop completely before reaching for anything.
Table saw - beyond the basics
The operations Tech 3-4 adds - and their rules:
Never trust the fence scale - measure blade-to-fence with your tape for anything that matters.
Dado and rabbet cuts usually mean removing the guard or riving knife - that is a teacher check-in, every single time , and the guard goes back on the moment the operation ends.
Swapping to a dado stack is a qualified-only, disconnected-first operation.
Know your wood: twisted or wet stock kicks back - flag it instead of forcing it.
Spot what’s wrong at the table saw
A classmate is about to rip a board. Tap the 4 problems before they start the cut.
Rip cut on the table saw - in order
Put a safe rip cut in order. Tap the first step, then the next…
Band saw
The curve machine for thick stock. Its specifics:
• Upper blade guide about 1/4 inch above the stock - an exposed blade is a cutting hazard and snaps easier.
• Hands to the sides of the cut line, never in line with the blade - push from beside the line, not behind it.
• Plan tight curves with relief cuts so the blade doesn’t bind.
• Never back out of a long curve with the blade running - it pulls the blade off the wheels. Stop the saw first.
• Blade stopped completely before clearing scraps off the table.
Band saw - resaw & drift
Resawing - cutting a board through its thickness into thinner boards - is a Tech 3-4 operation with its own setup:
A tall fence supports the board on edge; a featherboard keeps it there.
Slow, steady feed - resawing asks a lot of the blade; forcing it wanders and heats.
Drift is normal - band saw blades pull slightly off-line; steer with the stock, hands out of the blade’s line.
The thin offcut next to the blade gets pushed clear with a stick , never fingers.
Check blade tension and tracking before the first cut - a resaw finds every weakness a blade has.
Palm router
Small base, spinning cutter, strong opinions. Its specifics:
• Bit tight and fully seated (but not bottomed-out) in the collet - unplugged while you do it.
• Feed against the bit’s rotation - the correct direction lets you control the cut; feeding with the rotation lets the router yank itself along.
• Full speed before contact , then steady motion - pausing burns, forcing chatters.
• Small pieces get clamped , never hand-held under a router.
• Bits stay hot after cutting - let them cool before touching.
Band saw curve
Halfway through a long curve on the band saw, the blade starts to bind. You…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 31
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
31
ASK THE ROOM
Spot what’s wrong at the table saw
Stationary Machines
A classmate is about to rip a board. Tap the 4 problems before they start the cut.
Which items are hazards?
• Blade guard removed, sitting on the bench
• Hand pushing stock inches from the blade
• Cutting freehand - stock not against the fence
• Standing directly behind the stock
• Rip fence locked at the cut width
• Featherboard clamped to hold the stock
• Operator wearing safety glasses
Notes: Ask students to commit before advancing.
Prompt: A classmate is about to rip a board. Tap the 4 problems before they start the cut.
Blade guard removed, sitting on the bench: Guards stay on the machine, not next to it.
Hand pushing stock inches from the blade: That’s push-stick territory.
Cutting freehand - stock not against the fence: Freehand cuts on a table saw invite kickback.
Standing directly behind the stock: Kickback fires straight back - stand to the side.
Rip fence locked at the cut width: that’s exactly how straight rips are made.
Featherboard clamped to hold the stock: that’s good pressure toward the fence.
Operator wearing safety glasses: PPE is on - good.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 32
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
32
REVEAL
Spot what’s wrong at the table saw
Stationary Machines
HAZARDS
• Blade guard removed, sitting on the bench
• Hand pushing stock inches from the blade
• Cutting freehand - stock not against the fence
• Standing directly behind the stock
SAFE / CORRECT
• Rip fence locked at the cut width
• Featherboard clamped to hold the stock
• Operator wearing safety glasses
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Blade guard removed, sitting on the bench: Guards stay on the machine, not next to it.
Hand pushing stock inches from the blade: That’s push-stick territory.
Cutting freehand - stock not against the fence: Freehand cuts on a table saw invite kickback.
Standing directly behind the stock: Kickback fires straight back - stand to the side.
Rip fence locked at the cut width: that’s exactly how straight rips are made.
Featherboard clamped to hold the stock: that’s good pressure toward the fence.
Operator wearing safety glasses: PPE is on - good.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 33
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
33
ASK THE ROOM
Rip cut on the table saw - in order
Stationary Machines
Put a safe rip cut in order. Tap the first step, then the next…
Put the steps in the safest order.
• Let the blade stop before collecting the pieces
• Finish the narrow end with a push stick
• Feed the stock tight against the fence
• Check the guard and riving knife are in place
• Lock the rip fence at the cut width
• Set blade height - teeth just above the stock
Notes: Ask students to commit before advancing.
Prompt: Put a safe rip cut in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 34
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
34
REVEAL
Rip cut on the table saw - in order
Stationary Machines
CORRECT ORDER
• 1. Set blade height - teeth just above the stock
• 2. Lock the rip fence at the cut width
• 3. Check the guard and riving knife are in place
• 4. Feed the stock tight against the fence
• 5. Finish the narrow end with a push stick
• 6. Let the blade stop before collecting the pieces
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 35
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 10 OF 13
35
MODULE 10
Props Fabrication Equipment
3D printer, vacuum former, and casting & molding - heat and chemistry.
3D printer: Slow, quiet, and hot: The nozzle runs at 200°C+ and the bed is hot too - hands out of the machine while it prints and right after .
Vacuum former: A heating element hot enough to sag plastic - treat it that way: The heater and every fresh pull are burn-hot .
Casting, molding & resin: The chemistry corner.
5 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
3D printer
Slow, quiet, and hot:
The nozzle runs at 200°C+ and the bed is hot too - hands out of the machine while it prints and right after .
Don’t reach into the moving gantry - pause the print first.
Print in the ventilated space - melting filament off-gasses.
Removing supports: eye protection - snipped support bits fly, and fresh edges are sharp.
Vacuum former
A heating element hot enough to sag plastic - treat it that way:
The heater and every fresh pull are burn-hot . Gloves, or wait.
Never touch a sagging sheet - hot plastic drapes onto skin and sticks . That’s a serious burn, instantly.
Loose hair, sleeves, and lanyards stay away from the heater.
Trimming pulls uses your utility-knife rules : sharp blade, cut away, mat underneath.
Casting, molding & resin
The chemistry corner. Its specifics:
Gloves and ventilation, every time. Resins sensitize skin - each exposure makes the next reaction worse, and it’s permanent. “Just a little batch” counts.
Curing resin generates heat (exotherm) - large pours get genuinely hot; follow mix ratios and pour sizes.
Label and lid everything. Unlabeled chemicals are hazards twice: now and later.
Spills get cleaned immediately ; no food or drink anywhere near the casting bench.
Hot - or safe to touch?
Props equipment punishes the casual grab. Sort each one:
Resin check
You’re mixing a tiny batch of resin - thirty seconds of work. Gloves are across the room. Skip them?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 36
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
36
ASK THE ROOM
Hot - or safe to touch?
Props Fabrication Equipment
Props equipment punishes the casual grab. Sort each one:
Sort each item into: Hot - hands off / Safe to touch
• Printer nozzle right after a print finishes
• A vacuum-form pull fresh off the machine
• A resin part that cured yesterday
• Filament spools on the shelf
• The vac former’s heating element
Notes: Ask students to commit before advancing.
Prompt: Props equipment punishes the casual grab. Sort each one:
Printer nozzle right after a print finishes: 200°C+ and it looks exactly like a cold nozzle.
A vacuum-form pull fresh off the machine: Fresh pulls hold heat - gloves or wait.
A resin part that cured yesterday: Fully cured and cooled - fine.
Filament spools on the shelf: Just plastic until it meets the nozzle.
The vac former’s heating element: The hottest thing in the props area.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 37
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
37
REVEAL
Hot - or safe to touch?
Props Fabrication Equipment
Hot - hands off
• Printer nozzle right after a print finishes
• A vacuum-form pull fresh off the machine
• The vac former’s heating element
Safe to touch
• A resin part that cured yesterday
• Filament spools on the shelf
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Printer nozzle right after a print finishes: 200°C+ and it looks exactly like a cold nozzle.
A vacuum-form pull fresh off the machine: Fresh pulls hold heat - gloves or wait.
A resin part that cured yesterday: Fully cured and cooled - fine.
Filament spools on the shelf: Just plastic until it meets the nozzle.
The vac former’s heating element: The hottest thing in the props area.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 38
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
38
ASK THE ROOM
Resin check
Props Fabrication Equipment
You’re mixing a tiny batch of resin - thirty seconds of work. Gloves are across the room. Skip them?
Choose the safest response.
• A. Yes - it’s a tiny batch
• B. Yes, if you wash your hands right after
• C. No - resins sensitize skin, and every exposure counts
• D. Only skip them for clear resin
Notes: Ask students to commit before advancing.
Prompt: You’re mixing a tiny batch of resin - thirty seconds of work. Gloves are across the room. Skip them?
Sensitization is cumulative and permanent - the “quick batch” is exactly how it happens. Gloves every time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 39
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
39
REVEAL
Resin check
Props Fabrication Equipment
CORRECT ANSWER
• No - resins sensitize skin, and every exposure counts
WHY IT MATTERS
Sensitization is cumulative and permanent - the “quick batch” is exactly how it happens. Gloves every time.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Sensitization is cumulative and permanent - the “quick batch” is exactly how it happens. Gloves every time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 40
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 11 OF 13
40
MODULE 11
Lighting & Electrics
Ladders, fixture hardware, gels & gobos, cable care, hot focus, and electrical hazards.
Ladders & working at height: Know the ladder and working-at-height rules and be able to state them: • A ladder is set on stable ground and steadied - never climbed alone in the shop.
Power, plugs & equipment care: The rules for anything with a plug - consoles, playback, monitors, practicals: Dry hands only on switches, plugs, and equipment - and never use…
Cable care & over-under: Cable is equipment, not rope: Coil over-under so it pays out flat without kinks - a kinked cable is a damaged cable waiting to happen.
Lock-out / tag-out: When equipment is unsafe, it comes out of service - visibly : A tag (or lock) on a tool, cable, or machine means: dead until the instructor clears it .
Work like a professional: At this level you work at height and around power independently and safely - and you model the practices for everyone else: safety cable on every…
11 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Ladders & working at height
Know the ladder and working-at-height rules and be able to state them:
• A ladder is set on stable ground and steadied - never climbed alone in the shop.
• Keep three points of contact and never overreach; climb down and move the ladder instead.
• Nothing is carried up that can’t be carried safely; nothing gets dropped, ever.
Anyone working below wears the hazard in mind: if work is happening overhead, stay clear or call it out.
The hardware: C-clamp, wrench & safety cable
Your first lighting tools are hardware - and hardware has rules:
The wrench fits the bolt snugly - an adjustable wrench gets set tight; a loose fit rounds the bolt and skins knuckles.
Tighten the C-clamp snug, not gorilla-tight - over-torquing cracks clamps and pipes.
At height, the wrench is tethered or in a closed pocket - a dropped wrench from the grid is a missile with your name on the incident report.
The safety cable goes through the fixture’s yoke and around the pipe , clipped back on itself - so it catches the fixture even if the whole clamp lets go.
Power, plugs & equipment care
The rules for anything with a plug - consoles, playback, monitors, practicals:
Dry hands only on switches, plugs, and equipment - and never use electrical equipment near water or wet floors. Moisture conducts.
Before moving any equipment, disconnect and clear its cables. A dangling cord is a trip line and a broken connector.
Never defeat grounding - no forcing a three-prong plug into a two-prong outlet, ever. That third pin is what keeps a fault from going through you.
Connect gear only to the power type marked on it ; route cords where they can’t be walked on or pinched .
Give equipment ventilation - racks and amps cook when boxed in - and keep liquids and stray objects out of the openings.
Don’t service beyond the manual. Anything deeper goes to qualified personnel.
Gels, gobos & hot fronts
Handling the pretty parts safely:
Gels ride in gel frames - a loose gel stuffed in a fixture melts, smokes, and stinks up a performance.
Gobos are thin sharp steel - handle by the rim, like a razor-edged coin.
Warn everyone before switching an instrument on - nobody should be staring into a light that doesn’t announce itself.
Assume any instrument is extremely hot - even switched off. The front end (barrel, gel frame, shutters) holds burn heat long after the cue.
Keep instruments and flammable items apart - soft goods, paper, and scenery cook against a hot fixture.
Ask before touching any hung fixture - you don’t know how long it’s been running.
Cable care & over-under
Cable is equipment, not rope:
Coil over-under so it pays out flat without kinks - a kinked cable is a damaged cable waiting to happen.
Out of walkways , always - tape it down or reroute it.
Never yank a connector out by its cable - grip the connector itself.
Never pinch cable in doorways or run it over sharp edges .
Wet floors and cable don’t mix - dry first, then run power.
Hang a fixture - in order
Put the steps of hanging a fixture in order. Tap the first step, then the next…
Inspect before you use
You now work safely at height and around circuits with general supervision . That comes with a duty: inspect cables and fixtures before use - cracked connectors, frayed jacket, loose clamp, missing safety cable.
And when you find a fault, report it without prompting . A damaged cable that goes back in the bin unfixed is a trap for the next person.
Lock-out / tag-out
When equipment is unsafe, it comes out of service - visibly :
A tag (or lock) on a tool, cable, or machine means: dead until the instructor clears it . You don’t use it, you don’t “just test it,” and you never remove the tag.
That’s the student half of lock-out/tag-out - the industry system that keeps someone from powering up gear another person is working on.
The other half: your instructor inspects equipment weekly and documents it. Your pre-use inspection is the daily layer on top of that.
Hot focus
Refocusing fixtures that have been running is normal electrics work - done the right way:
Gloves for a hot fixture - or kill the channel and let it cool. A Source Four that’s been on all rehearsal blisters skin.
Loosen the right bolt - know your pan bolt from your tilt bolt so the unit moves where you expect instead of swinging free.
Wrench tethered or pocketed , same as every trip up the ladder.
Call your moves: “going into channel 12” - so the board op doesn’t light you up mid-grab.
Work like a professional
At this level you work at height and around power independently and safely - and you model the practices for everyone else: safety cable on every fixture, inspect before use, tag out and report faults immediately, never work an energized problem.
In Design & Management and Capstone work, you’re expected to bring these habits into any space you work in, without being told.
The energized problem
Halfway up the ladder you realize the fixture you’re about to re-lamp is still powered. What’s the professional move?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 41
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
41
ASK THE ROOM
Hang a fixture - in order
Lighting & Electrics
Put the steps of hanging a fixture in order. Tap the first step, then the next…
Put the steps in the safest order.
• Test it from the console
• Plug into the circuit
• Attach the safety cable
• Clamp it to the pipe and tighten the C-clamp
• Inspect the fixture and its cable
Notes: Ask students to commit before advancing.
Prompt: Put the steps of hanging a fixture in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 42
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
42
REVEAL
Hang a fixture - in order
Lighting & Electrics
CORRECT ORDER
• 1. Inspect the fixture and its cable
• 2. Clamp it to the pipe and tighten the C-clamp
• 3. Attach the safety cable
• 4. Plug into the circuit
• 5. Test it from the console
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 43
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 12 OF 13
43
MODULE 12
Rigging Safety
Wire rope, swaged terminations, and working load limits.
Wire rope & terminations: Anything flown or suspended rides on wire rope - never tie line or hope.
Working Load Limit (WLL): Every piece of rigging hardware - wire rope, shackles, clips - is rated with a Working Load Limit (WLL) : the maximum load it may safely carry.
4 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Wire rope & terminations
Anything flown or suspended rides on wire rope - never tie line or hope. You build wire-rope terminations to standard : a thimble protecting the loop, a Nicopress sleeve swaged with the correct tool, and every crimp checked with the gauge.
A termination that isn’t built to standard and verified does not take load. Ever.
Build a termination - in order
Put the steps of a wire-rope termination in order. Tap the first step, then the next…
Working Load Limit (WLL)
Every piece of rigging hardware - wire rope, shackles, clips - is rated with a Working Load Limit (WLL) : the maximum load it may safely carry.
You rig scenic elements within the WLL of every component in the system - the rig is only as strong as its weakest piece. Add up the real weight, know your ratings, and when in doubt, size up and ask.
The weakest link
Your rig uses wire rope rated 300 lb WLL, a shackle rated 250 lb , and a clip rated 100 lb . What is the most this system may carry?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 44
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
44
ASK THE ROOM
Build a termination - in order
Rigging Safety
Put the steps of a wire-rope termination in order. Tap the first step, then the next…
Put the steps in the safest order.
• Only now let it take load
• Check every crimp with the gauge
• Swage the sleeve with the crimping tool
• Slide the Nicopress sleeve over both parts of the rope
• Loop the wire rope around a thimble
Notes: Ask students to commit before advancing.
Prompt: Put the steps of a wire-rope termination in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 45
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
45
REVEAL
Build a termination - in order
Rigging Safety
CORRECT ORDER
• 1. Loop the wire rope around a thimble
• 2. Slide the Nicopress sleeve over both parts of the rope
• 3. Swage the sleeve with the crimping tool
• 4. Check every crimp with the gauge
• 5. Only now let it take load
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 46
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · MODULE 13 OF 13
46
MODULE 13
Hearing & Audio Safety
Hearing conservation, SPL awareness, and safe speaker handling.
Protect your hearing: Sound level is measured as SPL (sound pressure level).
Headsets & comms: The “no earbuds in the shop” rule has a show-business nuance: Personal earbuds and headphones never belong in the work environment - they mask callouts,…
Fog, haze & atmospherics: Atmosphere looks like magic and behaves like a chemical plus a slip hazard: Use only approved fluids in fog and haze machines - the fluid’s SDS lives in…
Handling & rigging speakers: Speakers are heavy, awkward, and often end up over people’s heads.
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Protect your hearing
Sound level is measured as SPL (sound pressure level). Loud sound damages the tiny hair cells in your inner ear - and that damage is cumulative and permanent . It never heals, it only adds up.
So: wear hearing protection around loud tools and loud playback, keep your distance from speakers at show level, and treat ringing ears as a warning you already went too far.
Ringing ears
After a loud work session, your ears are ringing. What does that mean?
Headsets & comms
The “no earbuds in the shop” rule has a show-business nuance:
Personal earbuds and headphones never belong in the work environment - they mask callouts, warnings, and the sound of trouble.
Production intercom is the exception - it exists so the crew can hear each other . Keep one ear open around moving scenery, keep chatter short and clean, and never let a joke on comms bury a “heads up.”
If you can’t hear the room, you’re not safe in the room.
Fog, haze & atmospherics
Atmosphere looks like magic and behaves like a chemical plus a slip hazard:
Use only approved fluids in fog and haze machines - the fluid’s SDS lives in the binder like every other chemical.
Heavy fog is a respiratory consideration - ventilation matters, and anyone with asthma should say so before the effect runs.
Fluid residue makes decks slick - watch the floor near the machine and mop drips.
Fog and haze can trip smoke alarms - effects run only with the instructor, coordinated with the venue.
The machine’s output and nozzle get hot .
Handling & rigging speakers
Speakers are heavy, awkward, and often end up over people’s heads.
• Lift and move them with help - protect your back and the cabinet.
• Anything flown or mounted overhead uses rated hardware and rigging points , secured so it cannot fall.
• Never stack or perch a speaker where a bump or a cable snag could bring it down.
Speakers: do - or never?
Sort each speaker move:
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 47
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
47
ASK THE ROOM
Ringing ears
Hearing & Audio Safety
After a loud work session, your ears are ringing. What does that mean?
Choose the safest response.
• A. Nothing - it fades, so no harm was done
• B. You already got too much sound; the damage adds up and doesn’t heal
• C. Your ears are getting stronger
• D. You should listen to quiet music to fix it
Notes: Ask students to commit before advancing.
Prompt: After a loud work session, your ears are ringing. What does that mean?
Ringing means overexposure. Hearing damage is cumulative and permanent - protect your ears earlier next time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 48
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · CLASSROOM CHECK
48
REVEAL
Ringing ears
Hearing & Audio Safety
CORRECT ANSWER
• You already got too much sound; the damage adds up and doesn’t heal
WHY IT MATTERS
Ringing means overexposure. Hearing damage is cumulative and permanent - protect your ears earlier next time.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Ringing means overexposure. Hearing damage is cumulative and permanent - protect your ears earlier next time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 49
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
49
ASK THE ROOM
Certification test check
Shop Safety & PPE
A task is going to fill the air with fine dust. Which PPE does that call for?
Choose the safest response.
• A. Hearing protection
• B. Dust protection, like a dust mask
• C. Just safety glasses
• D. Gloves
Notes: Ask students to commit before advancing.
Prompt: A task is going to fill the air with fine dust. Which PPE does that call for?
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 50
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
50
REVEAL
Certification test check
Shop Safety & PPE
CORRECT ANSWER
• Dust protection, like a dust mask
WHY IT MATTERS
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 51
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
51
ASK THE ROOM
Certification test check
Fire Safety & Emergencies
You discover a fire in the scene shop. What do you do first?
Choose the safest response.
• A. Shout “Fire!” as loudly as possible
• B. Immediately notify the closest adult with the exact location and what’s burning
• C. Look for a bucket of water
• D. Open the doors for ventilation
Notes: Ask students to commit before advancing.
Prompt: You discover a fire in the scene shop. What do you do first?
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 52
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
52
REVEAL
Certification test check
Fire Safety & Emergencies
CORRECT ANSWER
• Immediately notify the closest adult with the exact location and what’s burning
WHY IT MATTERS
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 53
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
53
ASK THE ROOM
Certification test check
Your Tools This Year
Which stationary machines are introduced in Tech 3-4 and require their own safety orientation?
Choose the safest response.
• A. Table saw, palm router, and band saw
• B. Jigsaw, impact driver, and sander
• C. 3D printer, vacuum former, and hot-wire knife
• D. Miter saw, panel saw, and framing nailer
Notes: Ask students to commit before advancing.
Prompt: Which stationary machines are introduced in Tech 3-4 and require their own safety orientation?
The table saw, palm router, and band saw are new at Grade 10 and each requires a safety orientation with direct supervision at first.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 54
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
54
REVEAL
Certification test check
Your Tools This Year
CORRECT ANSWER
• Table saw, palm router, and band saw
WHY IT MATTERS
The table saw, palm router, and band saw are new at Grade 10 and each requires a safety orientation with direct supervision at first.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
The table saw, palm router, and band saw are new at Grade 10 and each requires a safety orientation with direct supervision at first.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 55
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
55
ASK THE ROOM
Certification test check
Hand Tools & Knives
Which utility-knife blade is safer?
Choose the safest response.
• A. A dull one - it cuts more slowly
• B. A sharp one - it needs less force, so it slips less
• C. They’re the same
• D. Whichever one is already in the knife
Notes: Ask students to commit before advancing.
Prompt: Which utility-knife blade is safer?
Dull blades need force, and force is what slips - fresh, sharp blades are the safe ones.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 56
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
56
REVEAL
Certification test check
Hand Tools & Knives
CORRECT ANSWER
• A sharp one - it needs less force, so it slips less
WHY IT MATTERS
Dull blades need force, and force is what slips - fresh, sharp blades are the safe ones.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Dull blades need force, and force is what slips - fresh, sharp blades are the safe ones.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 57
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
57
ASK THE ROOM
Certification test check
Costume & Craft Tools
Where do pins live while you’re working?
Choose the safest response.
• A. In your lips, so they’re close
• B. Pinned to your sleeve
• C. In a pincushion or magnetic tray
• D. Loose on the table, next to the fabric
Notes: Ask students to commit before advancing.
Prompt: Where do pins live while you’re working?
Pins stay contained and countable - never in lips or clothes, and always counted back in at the end.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 58
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
58
REVEAL
Certification test check
Costume & Craft Tools
CORRECT ANSWER
• In a pincushion or magnetic tray
WHY IT MATTERS
Pins stay contained and countable - never in lips or clothes, and always counted back in at the end.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Pins stay contained and countable - never in lips or clothes, and always counted back in at the end.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 59
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
59
ASK THE ROOM
Certification test check
Power Tool Basics
The blade guard on the miter saw is sticking and won’t drop back over the blade. What do you do?
Choose the safest response.
• A. Use the saw carefully and keep your fingers back
• B. Tape the guard out of the way
• C. Stop, don’t use the saw, and report it
• D. Only make short cuts until it’s fixed
Notes: Ask students to commit before advancing.
Prompt: The blade guard on the miter saw is sticking and won’t drop back over the blade. What do you do?
A tool with a faulty guard never gets used - it gets reported and taken out of service.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 60
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
60
REVEAL
Certification test check
Power Tool Basics
CORRECT ANSWER
• Stop, don’t use the saw, and report it
WHY IT MATTERS
A tool with a faulty guard never gets used - it gets reported and taken out of service.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
A tool with a faulty guard never gets used - it gets reported and taken out of service.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 61
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
61
ASK THE ROOM
Certification test check
Power Saws: Jigsaw, Miter, Panel
You need a jigsaw cut in a small block of wood. The block gets…
Choose the safest response.
• A. Held firmly in your other hand
• B. Clamped to the bench
• C. Braced against your leg
• D. Held by a partner
Notes: Ask students to commit before advancing.
Prompt: You need a jigsaw cut in a small block of wood. The block gets…
Small pieces walk with the blade - and fingers follow. Clamp anything small.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 62
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
62
REVEAL
Certification test check
Power Saws: Jigsaw, Miter, Panel
CORRECT ANSWER
• Clamped to the bench
WHY IT MATTERS
Small pieces walk with the blade - and fingers follow. Clamp anything small.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Small pieces walk with the blade - and fingers follow. Clamp anything small.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 63
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
63
ASK THE ROOM
Certification test check
Drivers, Sanders & Nailers
You’re about to drive a nail about 2 inches from the hand bracing the stud. You…
Choose the safest response.
• A. Fire - nails go straight
• B. Use a shorter nail and fire
• C. Move your hand a full hand-span clear first
• D. Angle the nailer away from your hand slightly
Notes: Ask students to commit before advancing.
Prompt: You’re about to drive a nail about 2 inches from the hand bracing the stud. You…
Nails deflect along grain and off knots and can exit the wood sideways - clear the fire line before you shoot.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 64
SDSCPA
DESIGN & PRODUCTION · GRADE 10
SDSCPA · SAFETY LAB · GRADE 10 · TEST REVIEW
64
REVEAL
Certification test check
Drivers, Sanders & Nailers
CORRECT ANSWER
• Move your hand a full hand-span clear first
WHY IT MATTERS
Nails deflect along grain and off knots and can exit the wood sideways - clear the fire line before you shoot.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Nails deflect along grain and off knots and can exit the wood sideways - clear the fire line before you shoot.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 65
THEATRE SAFETY CERTIFICATION
GRADE 9
General supervision demands accurate setup and active problem reporting.
10 MODULES · 77 TRAINING SECTIONS · 12 CLASSROOM CHECKS
SDSCPA · SAFETY LAB · GRADE 9
65
Notes: Introduce the Grade 9 section and name the level of supervision students are working toward.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 66
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 01 OF 10
66
MODULE 01
Shop Safety & PPE
Dress code, hazards, PPE, lifting, housekeeping, emergencies, and safety culture.
Welcome to certification week: This week you earn your shop certification - proof that you know every rule and every tool you’re responsible for at your grade level, including…
Dress for the shop: Shop safety starts before you touch a tool - with what you’re wearing: Closed-toe shoes, every shop day.
Lifting & carrying: More shop injuries come from carrying than from cutting: Lift with your legs - squat, keep your back near-vertical, hug the load close, stand.
PPE without reminders: You’ve been introduced to PPE - now the bar is higher: select and wear the correct PPE for the task without being reminded .
Chemicals, SDS & the eyewash station: Paint, adhesives, solvents, and fog fluid are chemicals - and every chemical in the shop has a Safety Data Sheet (SDS) : The SDS binder lists each…
12 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Welcome to certification week
This week you earn your shop certification - proof that you know every rule and every tool you’re responsible for at your grade level, including everything from past years.
Plan on about 45 minutes of training a day : Days 1–4 are training modules, Day 5 is the certification quiz. The quiz needs 100% - and anything you miss sends you back to retrain that module. That’s not punishment; it’s how real shops qualify people.
Passing this lab is step one of the district’s safety program. Before you operate anything, your teacher still gives you hands-on demonstrations and a guided-practice sign-off on each piece of equipment - and nothing in this shop is ever operated without the instructor’s permission .
Permission & attention
The rule the district prints in capital letters: DO NOT OPERATE EQUIPMENT WITHOUT PERMISSION FROM THE INSTRUCTOR. Not before class, not during, not after - safety instruction and the instructor’s go-ahead come first, every time.
Keep your mind on the work. A moment of lost attention is how serious accidents happen.
No earbuds or headphones in the work environment - they mask warnings, callouts, and the sound of a machine going wrong. (Production intercom during shows is the one exception, used with discipline.)
When in doubt, ask the instructor - not the student next to you.
Dress for the shop
Shop safety starts before you touch a tool - with what you’re wearing:
Closed-toe shoes, every shop day. No sandals, no slides, no exceptions - dropped lumber doesn’t care how careful you were.
Long hair tied back. Hair near a spinning tool gets pulled in faster than you can react.
No dangling anything - jewelry, hoodie strings, loose sleeves, lanyards. If it hangs, it catches.
Sleeves rolled above the elbows , nothing loose at the wrists.
Gloves only where the task calls for them - rough lumber, hot fixtures, chemicals. Never around spinning blades or bits: a caught glove pulls the hand in with it.
No running, no horseplay. Ever. The shop is the one room where a joke shove can cost a finger.
Know your hazards
A theatre shop is full of things that can hurt you if you don’t see them coming: sharp tools and blades , things falling from above , dust in the air , loud noise , and cords, lumber, and clutter you can trip over .
Your first safety skill is simple: look around and name the hazards before you start any task. If you can’t name what could go wrong, you’re not ready to start.
Spot the hazards
Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Lifting & carrying
More shop injuries come from carrying than from cutting:
Lift with your legs - squat, keep your back near-vertical, hug the load close, stand. Your back is not a crane.
Never lift more than you can handle easily - over about 25 pounds, get help.
Clear your path before you pick anything up - most carrying accidents are collisions with things left on the floor or hanging at head height.
Team-lift anything long or heavy , and lift on a call: “ready - lift on three.” Same for setting down.
Carrying long stock: watch both ends , keep the front end high, and call the corners (“coming around!”).
Gloves for rough lumber - splinters are the tax on bare hands.
Watch the pinch points when setting anything down: fingers out from under, always.
Emergencies & injuries
Know these before you touch a single tool:
If anyone yells “STOP” or “HOLD” , all work stops instantly - no questions, hands off, tools down.
Every injury gets reported to the teacher immediately - no matter how slight - and an incident report is filed. A tiny cut in a dusty shop gets infected; a “small” incident often means a hazard that will hurt the next person worse.
Know where the first-aid kit lives.
Fire gets its own full module - alarms, exits, extinguisher classes, and how to report one.
PPE without reminders
You’ve been introduced to PPE - now the bar is higher: select and wear the correct PPE for the task without being reminded .
Safety glasses for cutting and drilling, hearing protection around loud tools, dust protection when sanding. Nobody should ever have to tell you. If you’re reaching for a tool, you’ve already reached for your PPE.
Pre-use check: good to go, or report it?
Before using any tool you do a pre-use safety check - and anything unsafe gets reported , even if it isn’t yours. Sort each finding:
Dust - the slow hazard
The hazard you can’t feel hurting you:
Fine wood dust harms lungs over years , not minutes - which is why nobody takes it seriously until it’s late. Take it seriously now.
Dust collection on whenever the sander or saws run.
Clean up dust by sweeping or vacuuming - never by blasting it airborne with the compressor.
The dust mask is for making dust and for cleaning it up .
The air hose is not a broom
You’re covered in sawdust after sanding, and the compressor hose is right there. Blow yourself off?
Chemicals, SDS & the eyewash station
Paint, adhesives, solvents, and fog fluid are chemicals - and every chemical in the shop has a Safety Data Sheet (SDS) :
The SDS binder lists each product’s hazards, handling rules, and first aid. Know where it lives.
Chemicals stay in labeled, closed containers - never in mystery cups or water bottles.
Rubber gloves are the exception to the no-gloves rule: wear them for stains, resins, and bleaches (never around spinning machines).
Know where the eyewash station is before you need it - you won’t be able to look for it with chemicals in your eyes.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 67
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
67
ASK THE ROOM
Spot the hazards
Shop Safety & PPE
Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Which items are hazards?
• Extension cord run across the walkway
• Hand saw left blade-up on the bench
• Boxes stacked in front of the exit
• Open drink next to the work area
• Board with a nail sticking out
• Safety glasses on the PPE shelf
• Fire extinguisher on its wall hook
• Swept floor, broom racked
Notes: Ask students to commit before advancing.
Prompt: Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Extension cord run across the walkway: Trip hazard - cords get routed out of walking paths.
Hand saw left blade-up on the bench: Sharp edges get sheathed or racked, never left out.
Boxes stacked in front of the exit: Exits stay clear - always.
Open drink next to the work area: Spills around tools and electricity - drinks stay out of the shop.
Board with a nail sticking out: Pull or bend nails the moment you see them.
Safety glasses on the PPE shelf: that’s exactly where PPE belongs.
Fire extinguisher on its wall hook: visible and ready - just right.
Swept floor, broom racked: good housekeeping is what prevents hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 68
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
68
REVEAL
Spot the hazards
Shop Safety & PPE
HAZARDS
• Extension cord run across the walkway
• Hand saw left blade-up on the bench
• Boxes stacked in front of the exit
• Open drink next to the work area
• Board with a nail sticking out
SAFE / CORRECT
• Safety glasses on the PPE shelf
• Fire extinguisher on its wall hook
• Swept floor, broom racked
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Extension cord run across the walkway: Trip hazard - cords get routed out of walking paths.
Hand saw left blade-up on the bench: Sharp edges get sheathed or racked, never left out.
Boxes stacked in front of the exit: Exits stay clear - always.
Open drink next to the work area: Spills around tools and electricity - drinks stay out of the shop.
Board with a nail sticking out: Pull or bend nails the moment you see them.
Safety glasses on the PPE shelf: that’s exactly where PPE belongs.
Fire extinguisher on its wall hook: visible and ready - just right.
Swept floor, broom racked: good housekeeping is what prevents hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 69
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 02 OF 10
69
MODULE 02
Fire Safety & Emergencies
Alarms, exits, extinguisher classes, reporting a fire, and flammable storage.
Alarms, drills & exits: Fire safety starts before there’s ever a fire: Know the fire bell/alarm and the fire-drill procedure for the shop and the theatre.
Reporting a fire: If you discover a fire: Immediately notify the closest adult with the exact location and the nature of the fire (what’s burning).
Fire classes & extinguishers: Extinguishers match the fire - the wrong one can make it worse: Class A - wood, paper, cloth.
Flammables, rags & finishes: The scene shop makes its own fire hazards: Rags soaked with finish, stain, or solvent go in a covered metal container - oily rags in a pile can…
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Alarms, drills & exits
Fire safety starts before there’s ever a fire:
Know the fire bell/alarm and the fire-drill procedure for the shop and the theatre.
Know every fire-exit location - and keep all exits and corridors clear at all times . In an evacuation, a blocked hallway costs lives, not minutes.
Know the types and locations of the fire extinguishers in your space - before you need them.
Reporting a fire
If you discover a fire:
Immediately notify the closest adult with the exact location and the nature of the fire (what’s burning).
Do NOT shout “Fire!” - panic in a crowded theatre is its own disaster; information moves faster than fear.
If someone’s clothing catches fire: smother the flames - get them down and roll them in a blanket if one is close.
Fire classes & extinguishers
Extinguishers match the fire - the wrong one can make it worse:
Class A - wood, paper, cloth. Water or CO₂ works.
Class B - flammable liquids (paint thinner, solvents). Smother it : foam or CO₂. Water spreads it.
Class C - electrical equipment. Non-conducting only : CO₂ or dry powder. Never water - electricity travels up the stream to you.
Pick the extinguisher
Match the fire to the response:
You spot smoke
You smell smoke and find a small fire behind the scene shop. What do you do first?
Flammables, rags & finishes
The scene shop makes its own fire hazards:
Rags soaked with finish, stain, or solvent go in a covered metal container - oily rags in a pile can self-ignite . That’s not a myth; it’s chemistry.
Use finishes and solvents only in well-ventilated areas, away from open flame and heat.
Keep flammable items away from lighting instruments - and instruments away from soft goods, paper, and scenery that could cook against a hot fixture.
Pyrotechnics, flame effects, and prop firearms are never student-operated - district approval and the fire marshal come first, every time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 70
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
70
ASK THE ROOM
Pick the extinguisher
Fire Safety & Emergencies
Match the fire to the response:
Sort each item into: Water works (Class A) / CO₂ / dry powder only
• Scrap lumber and paper burning in the bin
• A dimmer rack sparking and smoking
• Spilled paint thinner catches fire
• Muslin scraps smoldering in the paint corner
Notes: Ask students to commit before advancing.
Prompt: Match the fire to the response:
Scrap lumber and paper burning in the bin: Class A - ordinary combustibles; water or CO₂.
A dimmer rack sparking and smoking: Class C electrical - non-conducting extinguisher, never water.
Spilled paint thinner catches fire: Class B flammable liquid - smother with foam or CO₂; water spreads it.
Muslin scraps smoldering in the paint corner: Class A - cloth burns like paper.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 71
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
71
REVEAL
Pick the extinguisher
Fire Safety & Emergencies
Water works (Class A)
• Scrap lumber and paper burning in the bin
• Muslin scraps smoldering in the paint corner
CO₂ / dry powder only
• A dimmer rack sparking and smoking
• Spilled paint thinner catches fire
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Scrap lumber and paper burning in the bin: Class A - ordinary combustibles; water or CO₂.
A dimmer rack sparking and smoking: Class C electrical - non-conducting extinguisher, never water.
Spilled paint thinner catches fire: Class B flammable liquid - smother with foam or CO₂; water spreads it.
Muslin scraps smoldering in the paint corner: Class A - cloth burns like paper.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 72
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 03 OF 10
72
MODULE 03
Your Tools This Year
What’s new for you this year - and everything you carry forward.
Grade 9 - Tech 1-2: You now use the full hand-tool set , and your power tools move to general supervision : Power & pneumatic - jigsaw, compound miter saw, panel saw, impact…
2 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Grade 9 - Tech 1-2
You now use the full hand-tool set , and your power tools move to general supervision :
Power & pneumatic - jigsaw, compound miter saw, panel saw, impact driver, random orbital sander, narrow crown stapler, framing nailer.
Lighting - Source Four hang & focus tools (C-clamp, safety cable, wrench), cable; ETC Eos.
Costume - sewing machine.
Props - hot-wire foam knife.
Painting - brushes & rollers.
Cleared for you - or not yet?
Which of these are you cleared to use at your grade level (after passing each tool’s safety orientation)?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 73
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
73
ASK THE ROOM
Cleared for you - or not yet?
Your Tools This Year
Which of these are you cleared to use at your grade level (after passing each tool’s safety orientation)?
Sort each item into: Cleared for me / Not yet
• Compound miter saw
• Random orbital sander
• Framing nailer
• Table saw
• Band saw
• Palm router
Notes: Ask students to commit before advancing.
Prompt: Which of these are you cleared to use at your grade level (after passing each tool’s safety orientation)?
Compound miter saw: Yours after its safety orientation, with supervision.
Random orbital sander: Yours after its safety orientation, with supervision.
Framing nailer: Pneumatic tools are in - after the orientation.
Table saw: Stationary machines start in Grade 10.
Band saw: Stationary machines start in Grade 10.
Palm router: Stationary machines start in Grade 10.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 74
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
74
REVEAL
Cleared for you - or not yet?
Your Tools This Year
Cleared for me
• Compound miter saw
• Random orbital sander
• Framing nailer
Not yet
• Table saw
• Band saw
• Palm router
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Compound miter saw: Yours after its safety orientation, with supervision.
Random orbital sander: Yours after its safety orientation, with supervision.
Framing nailer: Pneumatic tools are in - after the orientation.
Table saw: Stationary machines start in Grade 10.
Band saw: Stationary machines start in Grade 10.
Palm router: Stationary machines start in Grade 10.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 75
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 04 OF 10
75
MODULE 04
Hand Tools & Knives
Tape measure, utility knife, squares, hammer, screwdrivers, hand saw - the tools everything else is built on.
Measuring & layout tools: Even “safe” tools have rules: Tape measure - control the blade on the way back in; a spring-loaded steel edge returning at full speed can cut.
Utility knife: The tool you’ll use most, and the one that sends the most people to the first-aid kit: • A sharp blade is safer than a dull one - it needs less force, so…
Hammer, screwdrivers & hand saw: Hammer - check the head is tight before swinging; clear your swing arc (people and your other hand); start nails with a light tap, fingers gone before…
Squares & layout at the bench: Layout tools earn their keep in Stagecraft: Speed square - your crosscut guide: hold it firm with your thumb up on its face, and run the saw along the…
7 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Measuring & layout tools
Even “safe” tools have rules:
Tape measure - control the blade on the way back in; a spring-loaded steel edge returning at full speed can cut. Watch the hook edge on long pulls.
Marking & layout tools - carry pointed tools (awls, compasses, pencils) tip-down , and never walk with them in a pocket point-up.
Every tool goes back to its rack when you set it down - a bench you can’t see the surface of is a bench hiding a blade.
Utility knife
The tool you’ll use most, and the one that sends the most people to the first-aid kit:
• A sharp blade is safer than a dull one - it needs less force, so it slips less. Swap dull blades.
• Cut away from your body - and away from the hand bracing the work. Ask: “if this slips, where does the blade finish?”
• Cut on a mat or scrap , never on the bare table or your knee.
• Retract the blade the second you stop cutting. No exceptions.
• Pass it handle-first , blade retracted. Used snap-off blades go in the taped sharps container, never loose in the trash.
Change a utility-knife blade - in order
Put a safe blade change in order. Tap the first step, then the next…
Hammer, screwdrivers & hand saw
Hammer - check the head is tight before swinging; clear your swing arc (people and your other hand); start nails with a light tap, fingers gone before the real swing.
Screwdrivers - use the right size tip so it doesn’t cam out; never drive toward your palm or hold the work in your hand; a screwdriver is not a chisel or a pry bar - tips snap and hands slip.
Hand saw - start the kerf with short, light strokes; keep your free hand clear of the cut line; support the off-cut so it doesn’t tear free at the end.
Squares & layout at the bench
Layout tools earn their keep in Stagecraft:
Speed square - your crosscut guide: hold it firm with your thumb up on its face, and run the saw along the edge. Fingers stay on top of the square, never on the blade side.
Framing square - for sheet layout and checking corners; two people hold it for long lines.
Mark the waste side of every line with an X - half the “wrong cuts” in a shop are right cuts on the wrong side.
A sharp pencil line beats a fat one; for fine work, a knife line beats both (utility-knife rules apply).
Hand-tool habits
Sort each habit:
Make a hand-saw cut - in order
Put a clean, safe hand-saw cut in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 76
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
76
ASK THE ROOM
Change a utility-knife blade - in order
Hand Tools & Knives
Put a safe blade change in order. Tap the first step, then the next…
Put the steps in the safest order.
• Test the slider and lock before cutting
• Seat the new blade and close the knife
• Old blade goes into the taped sharps container
• Open the knife and lift out the old blade
• Retract the blade fully
Notes: Ask students to commit before advancing.
Prompt: Put a safe blade change in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 77
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
77
REVEAL
Change a utility-knife blade - in order
Hand Tools & Knives
CORRECT ORDER
• 1. Retract the blade fully
• 2. Open the knife and lift out the old blade
• 3. Old blade goes into the taped sharps container
• 4. Seat the new blade and close the knife
• 5. Test the slider and lock before cutting
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 78
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 05 OF 10
78
MODULE 05
Costume & Craft Tools
Needles, pins, shears, papier-mâché & armatures, the sewing machine, and the hot-wire foam knife.
Needles, pins & hand sewing: Small tools, real rules: Count your needles and pins out - and back in.
Scissors & pattern tools: Fabric shears are seriously sharp - that’s the point.
Papier-mâché & armatures: Props building has its own sharp ends: Cut armature wire with wire cutters, never scissors - scissors get ruined, and ruined tools slip.
Sewing machine: The machine drives a needle up and down faster than you can react - respect the zone around it: • Fingers stay a needle-width away - guide fabric from…
Hot-wire foam knife: It doesn’t look dangerous - it’s a wire.
8 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Needles, pins & hand sewing
Small tools, real rules:
Count your needles and pins out - and back in. A lost pin ends up in a costume, a couch, or a foot.
Pins live in a pincushion or magnetic tray - never in your lips, never in your clothes.
Broken needles and bent pins get taped and binned , not tossed loose.
Anything sharp gets passed handle-first .
Scissors & pattern tools
Fabric shears are seriously sharp - that’s the point.
• Carry them closed, point-down . Never run - it’s a cliché because it’s true.
• Pass them handle-first .
• Cut on the table , fabric flat, free hand behind the blades - not in the air toward yourself.
• Fabric shears cut fabric only : paper and cardboard dull them into tools that slip.
Papier-mâché & armatures
Props building has its own sharp ends:
Cut armature wire with wire cutters, never scissors - scissors get ruined, and ruined tools slip.
Every cut wire end gets bent back or taped immediately. Armature wires stick out at exactly eye height on a crowded work table.
Paste makes floors slick - wipe drips when they happen, not at cleanup.
Cover cuts on your hands before pasting, and wash up after - paste and sealers aren’t hand lotion.
Wire ends
You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Sewing machine
The machine drives a needle up and down faster than you can react - respect the zone around it:
• Fingers stay a needle-width away - guide fabric from the sides, never push it from directly in front of the needle.
• No loose sleeves, jewelry, or hair near the needle and handwheel.
• Control speed with the pedal - start slow ; speed is earned, not assumed.
• Power off (or unplug) before changing the needle or working close to it.
• Let the machine stop completely before reaching in to pull threads or fabric.
Sewing machine check
The needle on your machine is bent and needs changing. First move?
Hot-wire foam knife
It doesn’t look dangerous - it’s a wire. But it cuts by heat :
The wire burns skin instantly and stays hot after you switch it off - it rests on its stand until cool.
Only cut approved foam (polystyrene). Unknown foams and polyurethane can release toxic fumes when hot. If you don’t know what the foam is, you don’t cut it.
Cut with ventilation on , away from anything flammable.
A burn gets cool water and gets reported - like every injury.
Hot-wire check
A scrap of foam with no label shows up in the bin, and it would be perfect for your prop. Hot-wire it?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 79
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
79
ASK THE ROOM
Wire ends
Costume & Craft Tools
You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Choose the safest response.
• A. Finish the layer first, then deal with it
• B. Bend it back or tape it immediately
• C. Point it out to the people nearby
• D. Move your own face away from it
Notes: Ask students to commit before advancing.
Prompt: You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 80
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
80
REVEAL
Wire ends
Costume & Craft Tools
CORRECT ANSWER
• Bend it back or tape it immediately
WHY IT MATTERS
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 81
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 06 OF 10
81
MODULE 06
Power Tool Basics
The rules that cover every power and pneumatic tool, and your path to qualification.
Rules that never change: For every power and pneumatic tool, at every grade level: • Guards stay on and working.
Your path: orientation → supervision → independence: Qualification is a ladder, and every tool has its own rung: 1⃣ Safety orientation (Grade 8) - you pass an orientation for each tool, then perform…
Cords, hoses & your workspace: The cable end of tool safety: The cord or hose stays behind the tool, never in the cut path - check before every cut, not after.
Clamp it, support it: Most “tool accidents” are really workholding accidents : A clamp beats your strongest grip - and it never flinches.
Pneumatic power: the air rules: The stapler and nailer run on compressed air, which adds rules of their own: • Treat every air tool as loaded.
9 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Rules that never change
For every power and pneumatic tool, at every grade level:
• Guards stay on and working. A tool with a faulty guard doesn’t get used - it gets reported.
• PPE first - safety glasses always; hearing and dust protection as the task demands.
• Correct body position - balanced stance, hands clear of the cut line, never reaching across a blade.
• Disconnect power or air before adjusting - blade changes, depth settings, or clearing jams happen only on a dead tool.
Your path: orientation → supervision → independence
Qualification is a ladder, and every tool has its own rung:
1⃣ Safety orientation (Grade 8) - you pass an orientation for each tool, then perform fundamental operations under direct supervision : straight cuts, crosscuts, driving fasteners, sanding flat stock.
2⃣ General supervision (Grade 9) - you set up and operate each tool with the teacher in the shop, not at your elbow, producing accurate cuts and secure assemblies.
3⃣ Independent qualification (Grade 10+) - you pass an independent-use qualification per tool, handle routine adjustments yourself, and help train peers.
Grade level alone never qualifies you - passing the orientation or qualification for that specific tool does .
Notice and report
From Grade 9 on, noticing problems is part of your qualification :
• A blade that burns the wood or cuts slowly is dull - stop and report it.
• A pneumatic tool that sputters or double-fires may have low or wrong air pressure - stop and report it.
• Anything loose, cracked, wobbling, or smelling hot - stop and report it .
You are not “bothering the teacher.” You are doing the job.
Cords, hoses & your workspace
The cable end of tool safety:
The cord or hose stays behind the tool, never in the cut path - check before every cut, not after.
Never carry a tool by its cord , and unplug by gripping the plug , not yanking the cable.
Disconnecting an air hose: shut off the air and bleed the pressure first , and keep hold of the coupling - a charged hose whips.
Cords and hoses route along walls and out of walkways , same as the shop rule you already know.
Clamp it, support it
Most “tool accidents” are really workholding accidents :
A clamp beats your strongest grip - and it never flinches.
Long stock gets outfeed support - a sawhorse, a stand, or a partner on a callout.
The cut line hangs clear of the bench - cutting into the table pinches the blade and ruins both.
Never cut work resting on your knee or held in the air.
Know what’s under and behind the cut before you start it.
Set up a cut - in order
Put the steps of a safe power-tool cut in order. Tap the first step, then the next…
Pneumatic power: the air rules
The stapler and nailer run on compressed air, which adds rules of their own:
• Treat every air tool as loaded. Finger off the trigger until the nose is on the work.
• Never point one at anyone - including yourself. Ever. Even “empty.”
• Disconnect the air line before clearing a jam, adjusting, or handing it over.
• Use the tool’s correct air pressure - too high blows fasteners through the work; too low jams and double-fires.
• Hoses get routed out of walkways , like every cord.
Jammed nailer
The framing nailer jams mid-wall. Before you touch the jam, you…
Cord in the lane
Mid-setup, you notice the jigsaw’s own cord crossing under the line you’re about to cut. You…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 82
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
82
ASK THE ROOM
Set up a cut - in order
Power Tool Basics
Put the steps of a safe power-tool cut in order. Tap the first step, then the next…
Put the steps in the safest order.
• Let the blade stop completely before reaching in
• Make the cut with correct body position
• Clear the work area and support your stock
• Check guards, blade, and cord or hose
• Put on your PPE
Notes: Ask students to commit before advancing.
Prompt: Put the steps of a safe power-tool cut in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 83
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
83
REVEAL
Set up a cut - in order
Power Tool Basics
CORRECT ORDER
• 1. Put on your PPE
• 2. Check guards, blade, and cord or hose
• 3. Clear the work area and support your stock
• 4. Make the cut with correct body position
• 5. Let the blade stop completely before reaching in
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 84
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 07 OF 10
84
MODULE 07
Power Saws: Jigsaw, Miter, Panel
Tool-by-tool specifics for the three saws you qualified on in Stagecraft.
Jigsaw: The curve-cutter.
Jigsaw - blades, curves & cutouts: Getting the cut you want, safely: Match the blade to the material - wood, metal, and scroll blades are different animals; the wrong one burns, wanders,…
Miter saw - angles & short stock: The setups that catch people: Set and lock the angle , then test on scrap - an unlocked table creeps mid-cut.
Panel saw: The sheet-goods saw.
Rip vs crosscut - know your cut: Two words you’ll hear every day in the shop: A crosscut goes across the grain - cutting a 2×4 to length.
11 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Jigsaw
The curve-cutter. Its specifics:
• Clamp your stock - small pieces walk with the blade and take fingers along.
• Base plate flat on the work before you pull the trigger.
• Know what’s under the cut - the blade sticks out below the stock. Nothing under the line: not the bench edge, not the cord, not your hand.
• Let the blade stop before lifting the saw out of the cut.
• Forcing the cut bends and snaps blades - let the blade do the work . Unplug to change blades.
Jigsaw - blades, curves & cutouts
Getting the cut you want, safely:
Match the blade to the material - wood, metal, and scroll blades are different animals; the wrong one burns, wanders, and snaps.
Tight curves want narrow blades - and really tight curves want relief cuts first, so the blade never binds.
Interior cutouts start from a drilled starter hole , never from tipping the saw into the surface.
A blade that starts wandering off your line is worn out - swap it (unplugged) instead of steering harder.
Compound miter saw
The crosscut machine. Its specifics:
• Stock tight against the fence - always. A gap lets the blade grab and slam the stock.
• Hands outside the no-hand zone (at least 6 inches from the blade path). Never cross your arms - left hand holding the right side of the blade is how people meet the blade.
• Full speed before the cut - let it spin up, then bring it down smoothly.
• After the cut, keep the blade down until it stops - a spinning blade coming up can grab the off-cut and throw it.
• Support long stock on both ends; never balance it.
Miter saw - angles & short stock
The setups that catch people:
Set and lock the angle , then test on scrap - an unlocked table creeps mid-cut.
Long stock gets a stand or a partner (on a callout) at the far end - a see-sawing board pinches the blade.
Anything too short to hold outside the no-hand zone gets clamped - or cut from a longer board so your hand never gets close.
If a cut would put your fingers inside the zone, that cut doesn’t happen that way. There is always another way.
Miter saw check
You just finished a cut on the miter saw. When do you raise the blade?
The short piece
You need a 3-inch block. Holding it for the miter cut would put your fingers inside the no-hand zone. You…
Panel saw
The sheet-goods saw. Its specifics:
• Seat the sheet fully on the rollers/rails before cutting - a cocked sheet binds the blade.
• Both hands on the carriage handle. Never steady the sheet with a hand near the cut line.
• Let the carriage return home before touching anything.
• Mind the off-cut - full sheets are heavy, and freed panels pinch fingers and toes. Get help catching big pieces.
Panel saw sheet cut - in order
Put a full-sheet cut on the panel saw in order. Tap the first step, then the next…
Rip vs crosscut - know your cut
Two words you’ll hear every day in the shop:
A crosscut goes across the grain - cutting a 2×4 to length. That’s the miter saw’s job.
A rip cut runs along the grain or the length of a sheet. At your grade, sheet rips happen on the panel saw .
The table saw - the shop’s main rip machine - waits for Grade 10 and its own orientation.
Naming the cut tells you the tool; the tool tells you the rules.
Which saw for the job?
Choosing the right saw is a safety skill - the wrong tool fights you. Match each cut to its saw:
Spot what’s wrong: the cutting station
Walk the saw stations and tap the 4 problems .
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 85
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
85
ASK THE ROOM
Miter saw check
Power Saws: Jigsaw, Miter, Panel
You just finished a cut on the miter saw. When do you raise the blade?
Choose the safest response.
• A. Immediately - the cut is done
• B. After the blade has stopped spinning
• C. Once the off-cut falls clear
• D. After you pull the stock away
Notes: Ask students to commit before advancing.
Prompt: You just finished a cut on the miter saw. When do you raise the blade?
A spinning blade coming up can catch the off-cut and throw it - the blade stays down until it stops.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 86
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
86
REVEAL
Miter saw check
Power Saws: Jigsaw, Miter, Panel
CORRECT ANSWER
• After the blade has stopped spinning
WHY IT MATTERS
A spinning blade coming up can catch the off-cut and throw it - the blade stays down until it stops.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
A spinning blade coming up can catch the off-cut and throw it - the blade stays down until it stops.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 87
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 08 OF 10
87
MODULE 08
Drivers, Sanders & Nailers
Impact driver, random orbital sander, narrow crown stapler, and framing nailer.
Impact driver: Small tool, huge torque.
Bits & torque: The details that separate clean driving from stripped screws: Right bit, right size - a PH2 in a PH3 screw strips both.
Random orbital sander: The dust machine.
Grits & technique: Sanding well is sanding safely - fighting the tool is what causes slips: Work the grit ladder: 80 → 120 → 220 .
Stapler & framing nailer: You learned the air rules in Power Tool Basics - here are the gun-specific ones: • The contact safety tip on the nose is what stops accidental fires.
7 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Impact driver
Small tool, huge torque. Its specifics:
• Seat the bit fully in the screw head before pulling the trigger - a half-seated bit cams out and skates.
• Hand off the fastener line. When the bit slips, it goes exactly where your hand was going to be.
• Start slow to set the threads, then run it home.
• Brace small work - the driver will happily spin the workpiece instead of the screw.
• Eye protection: screw heads snap and bits shatter.
Bits & torque
The details that separate clean driving from stripped screws:
Right bit, right size - a PH2 in a PH3 screw strips both. Check before you drive.
Worn bits get binned , not babied - a rounded bit cams out no matter how hard you push.
Impact drivers hammer - that rattle is the mechanism working, and it’s loud : hearing protection when the driving runs long.
Small screws snap under full impact - ease off as the head seats.
Pilot holes near edges stop the split before it starts.
Random orbital sander
The dust machine. Its specifics:
• Dust protection on, dust collection attached - fine dust is the hazard you can’t see hurting you.
• Don’t press. The tool’s weight is enough; leaning on it burns the paper, scorches the stock, and stalls the pad.
• Let the pad stop before you set it down - a live sander walks off the bench.
• Secure small pieces ; the sander is strong enough to launch them.
• Keep the cord behind the tool , never under the pad.
Grits & technique
Sanding well is sanding safely - fighting the tool is what causes slips:
Work the grit ladder: 80 → 120 → 220 . Skipping grits means pressing harder for less result.
Keep the pad flat and moving - parking it in one spot digs a dish you’ll sand an hour to fix.
Edges round over in seconds - ease up when you get near them.
Let the paper do the work: if you’re pressing, the paper’s done - change it .
Stapler & framing nailer
You learned the air rules in Power Tool Basics - here are the gun-specific ones:
• The contact safety tip on the nose is what stops accidental fires. It is never held down, taped, or bypassed . Never.
• Sequential fire : nose on the work first, then the trigger.
• Hands at least a hand-span from the fire line. Staples and nails follow the grain and deflect off knots - they can exit the wood sideways .
• The framing nailer recoils - grip it, expect it.
• Carry with your finger off the trigger ; disconnect air to clear jams or hand it off.
Nailer check
Your palm is bracing a stud about 2 inches from where you’re about to shoot a nail. Fire?
Driver & sander habits
Sort each habit:
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 88
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
88
ASK THE ROOM
Nailer check
Drivers, Sanders & Nailers
Your palm is bracing a stud about 2 inches from where you’re about to shoot a nail. Fire?
Choose the safest response.
• A. Yes - the nail goes straight down
• B. Yes, if you use a shorter nail
• C. No - move your hand first; nails deflect along grain and knots and can exit sideways
• D. No - you should hold the stud closer to the nail for control
Notes: Ask students to commit before advancing.
Prompt: Your palm is bracing a stud about 2 inches from where you’re about to shoot a nail. Fire?
Nails follow the grain and bounce off knots - a hand-span of clearance from the fire line, minimum.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 89
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · CLASSROOM CHECK
89
REVEAL
Nailer check
Drivers, Sanders & Nailers
CORRECT ANSWER
• No - move your hand first; nails deflect along grain and knots and can exit sideways
WHY IT MATTERS
Nails follow the grain and bounce off knots - a hand-span of clearance from the fire line, minimum.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Nails follow the grain and bounce off knots - a hand-span of clearance from the fire line, minimum.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 90
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 09 OF 10
90
MODULE 09
Lighting & Electrics
Ladders, fixture hardware, gels & gobos, cable care, hot focus, and electrical hazards.
Ladders & working at height: Know the ladder and working-at-height rules and be able to state them: • A ladder is set on stable ground and steadied - never climbed alone in the shop.
Power, plugs & equipment care: The rules for anything with a plug - consoles, playback, monitors, practicals: Dry hands only on switches, plugs, and equipment - and never use…
Cable care & over-under: Cable is equipment, not rope: Coil over-under so it pays out flat without kinks - a kinked cable is a damaged cable waiting to happen.
Inspect before you use: You now work safely at height and around circuits with general supervision .
Hot focus: Refocusing fixtures that have been running is normal electrics work - done the right way: Gloves for a hot fixture - or kill the channel and let it cool.
9 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Ladders & working at height
Know the ladder and working-at-height rules and be able to state them:
• A ladder is set on stable ground and steadied - never climbed alone in the shop.
• Keep three points of contact and never overreach; climb down and move the ladder instead.
• Nothing is carried up that can’t be carried safely; nothing gets dropped, ever.
Anyone working below wears the hazard in mind: if work is happening overhead, stay clear or call it out.
The hardware: C-clamp, wrench & safety cable
Your first lighting tools are hardware - and hardware has rules:
The wrench fits the bolt snugly - an adjustable wrench gets set tight; a loose fit rounds the bolt and skins knuckles.
Tighten the C-clamp snug, not gorilla-tight - over-torquing cracks clamps and pipes.
At height, the wrench is tethered or in a closed pocket - a dropped wrench from the grid is a missile with your name on the incident report.
The safety cable goes through the fixture’s yoke and around the pipe , clipped back on itself - so it catches the fixture even if the whole clamp lets go.
Power, plugs & equipment care
The rules for anything with a plug - consoles, playback, monitors, practicals:
Dry hands only on switches, plugs, and equipment - and never use electrical equipment near water or wet floors. Moisture conducts.
Before moving any equipment, disconnect and clear its cables. A dangling cord is a trip line and a broken connector.
Never defeat grounding - no forcing a three-prong plug into a two-prong outlet, ever. That third pin is what keeps a fault from going through you.
Connect gear only to the power type marked on it ; route cords where they can’t be walked on or pinched .
Give equipment ventilation - racks and amps cook when boxed in - and keep liquids and stray objects out of the openings.
Don’t service beyond the manual. Anything deeper goes to qualified personnel.
Gels, gobos & hot fronts
Handling the pretty parts safely:
Gels ride in gel frames - a loose gel stuffed in a fixture melts, smokes, and stinks up a performance.
Gobos are thin sharp steel - handle by the rim, like a razor-edged coin.
Warn everyone before switching an instrument on - nobody should be staring into a light that doesn’t announce itself.
Assume any instrument is extremely hot - even switched off. The front end (barrel, gel frame, shutters) holds burn heat long after the cue.
Keep instruments and flammable items apart - soft goods, paper, and scenery cook against a hot fixture.
Ask before touching any hung fixture - you don’t know how long it’s been running.
Cable care & over-under
Cable is equipment, not rope:
Coil over-under so it pays out flat without kinks - a kinked cable is a damaged cable waiting to happen.
Out of walkways , always - tape it down or reroute it.
Never yank a connector out by its cable - grip the connector itself.
Never pinch cable in doorways or run it over sharp edges .
Wet floors and cable don’t mix - dry first, then run power.
Hang a fixture - in order
Put the steps of hanging a fixture in order. Tap the first step, then the next…
Inspect before you use
You now work safely at height and around circuits with general supervision . That comes with a duty: inspect cables and fixtures before use - cracked connectors, frayed jacket, loose clamp, missing safety cable.
And when you find a fault, report it without prompting . A damaged cable that goes back in the bin unfixed is a trap for the next person.
Lock-out / tag-out
When equipment is unsafe, it comes out of service - visibly :
A tag (or lock) on a tool, cable, or machine means: dead until the instructor clears it . You don’t use it, you don’t “just test it,” and you never remove the tag.
That’s the student half of lock-out/tag-out - the industry system that keeps someone from powering up gear another person is working on.
The other half: your instructor inspects equipment weekly and documents it. Your pre-use inspection is the daily layer on top of that.
Hot focus
Refocusing fixtures that have been running is normal electrics work - done the right way:
Gloves for a hot fixture - or kill the channel and let it cool. A Source Four that’s been on all rehearsal blisters skin.
Loosen the right bolt - know your pan bolt from your tilt bolt so the unit moves where you expect instead of swinging free.
Wrench tethered or pocketed , same as every trip up the ladder.
Call your moves: “going into channel 12” - so the board op doesn’t light you up mid-grab.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 91
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · MODULE 10 OF 10
91
MODULE 10
Hearing & Audio Safety
Hearing conservation, SPL awareness, and safe speaker handling.
Protect your hearing: Sound level is measured as SPL (sound pressure level).
Headsets & comms: The “no earbuds in the shop” rule has a show-business nuance: Personal earbuds and headphones never belong in the work environment - they mask callouts,…
Fog, haze & atmospherics: Atmosphere looks like magic and behaves like a chemical plus a slip hazard: Use only approved fluids in fog and haze machines - the fluid’s SDS lives in…
Handling & rigging speakers: Speakers are heavy, awkward, and often end up over people’s heads.
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Protect your hearing
Sound level is measured as SPL (sound pressure level). Loud sound damages the tiny hair cells in your inner ear - and that damage is cumulative and permanent . It never heals, it only adds up.
So: wear hearing protection around loud tools and loud playback, keep your distance from speakers at show level, and treat ringing ears as a warning you already went too far.
Ringing ears
After a loud work session, your ears are ringing. What does that mean?
Headsets & comms
The “no earbuds in the shop” rule has a show-business nuance:
Personal earbuds and headphones never belong in the work environment - they mask callouts, warnings, and the sound of trouble.
Production intercom is the exception - it exists so the crew can hear each other . Keep one ear open around moving scenery, keep chatter short and clean, and never let a joke on comms bury a “heads up.”
If you can’t hear the room, you’re not safe in the room.
Fog, haze & atmospherics
Atmosphere looks like magic and behaves like a chemical plus a slip hazard:
Use only approved fluids in fog and haze machines - the fluid’s SDS lives in the binder like every other chemical.
Heavy fog is a respiratory consideration - ventilation matters, and anyone with asthma should say so before the effect runs.
Fluid residue makes decks slick - watch the floor near the machine and mop drips.
Fog and haze can trip smoke alarms - effects run only with the instructor, coordinated with the venue.
The machine’s output and nozzle get hot .
Handling & rigging speakers
Speakers are heavy, awkward, and often end up over people’s heads.
• Lift and move them with help - protect your back and the cabinet.
• Anything flown or mounted overhead uses rated hardware and rigging points , secured so it cannot fall.
• Never stack or perch a speaker where a bump or a cable snag could bring it down.
Speakers: do - or never?
Sort each speaker move:
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 92
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
92
ASK THE ROOM
Certification test check
Shop Safety & PPE
A task is going to fill the air with fine dust. Which PPE does that call for?
Choose the safest response.
• A. Hearing protection
• B. Dust protection, like a dust mask
• C. Just safety glasses
• D. Gloves
Notes: Ask students to commit before advancing.
Prompt: A task is going to fill the air with fine dust. Which PPE does that call for?
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 93
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
93
REVEAL
Certification test check
Shop Safety & PPE
CORRECT ANSWER
• Dust protection, like a dust mask
WHY IT MATTERS
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 94
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
94
ASK THE ROOM
Certification test check
Fire Safety & Emergencies
You discover a fire in the scene shop. What do you do first?
Choose the safest response.
• A. Shout “Fire!” as loudly as possible
• B. Immediately notify the closest adult with the exact location and what’s burning
• C. Look for a bucket of water
• D. Open the doors for ventilation
Notes: Ask students to commit before advancing.
Prompt: You discover a fire in the scene shop. What do you do first?
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 95
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
95
REVEAL
Certification test check
Fire Safety & Emergencies
CORRECT ANSWER
• Immediately notify the closest adult with the exact location and what’s burning
WHY IT MATTERS
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 96
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
96
ASK THE ROOM
Certification test check
Your Tools This Year
Before using any power or pneumatic tool for the first time, you must…
Choose the safest response.
• A. Watch one other student use it
• B. Pass a safety orientation for that specific tool
• C. Just start on scrap wood
• D. Get permission from any older student
Notes: Ask students to commit before advancing.
Prompt: Before using any power or pneumatic tool for the first time, you must…
Every power and pneumatic tool requires passing its own safety orientation before you use it.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 97
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
97
REVEAL
Certification test check
Your Tools This Year
CORRECT ANSWER
• Pass a safety orientation for that specific tool
WHY IT MATTERS
Every power and pneumatic tool requires passing its own safety orientation before you use it.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Every power and pneumatic tool requires passing its own safety orientation before you use it.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 98
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
98
ASK THE ROOM
Certification test check
Hand Tools & Knives
Which utility-knife blade is safer?
Choose the safest response.
• A. A dull one - it cuts more slowly
• B. A sharp one - it needs less force, so it slips less
• C. They’re the same
• D. Whichever one is already in the knife
Notes: Ask students to commit before advancing.
Prompt: Which utility-knife blade is safer?
Dull blades need force, and force is what slips - fresh, sharp blades are the safe ones.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 99
SDSCPA
DESIGN & PRODUCTION · GRADE 9
SDSCPA · SAFETY LAB · GRADE 9 · TEST REVIEW
99
REVEAL
Certification test check
Hand Tools & Knives
CORRECT ANSWER
• A sharp one - it needs less force, so it slips less
WHY IT MATTERS
Dull blades need force, and force is what slips - fresh, sharp blades are the safe ones.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Dull blades need force, and force is what slips - fresh, sharp blades are the safe ones.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 100
THEATRE SAFETY CERTIFICATION
GRADE 8
Direct supervision starts with repeatable habits and clear communication.
10 MODULES · 72 TRAINING SECTIONS · 9 CLASSROOM CHECKS
SDSCPA · SAFETY LAB · GRADE 8
100
Notes: Introduce the Grade 8 section and name the level of supervision students are working toward.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 101
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 01 OF 10
101
MODULE 01
Shop Safety & PPE
Dress code, hazards, PPE, lifting, housekeeping, emergencies, and safety culture.
Welcome to certification week: This week you earn your shop certification - proof that you know every rule and every tool you’re responsible for at your grade level, including…
Dress for the shop: Shop safety starts before you touch a tool - with what you’re wearing: Closed-toe shoes, every shop day.
Lifting & carrying: More shop injuries come from carrying than from cutting: Lift with your legs - squat, keep your back near-vertical, hug the load close, stand.
PPE without reminders: You’ve been introduced to PPE - now the bar is higher: select and wear the correct PPE for the task without being reminded .
Chemicals, SDS & the eyewash station: Paint, adhesives, solvents, and fog fluid are chemicals - and every chemical in the shop has a Safety Data Sheet (SDS) : The SDS binder lists each…
12 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Welcome to certification week
This week you earn your shop certification - proof that you know every rule and every tool you’re responsible for at your grade level, including everything from past years.
Plan on about 45 minutes of training a day : Days 1–4 are training modules, Day 5 is the certification quiz. The quiz needs 100% - and anything you miss sends you back to retrain that module. That’s not punishment; it’s how real shops qualify people.
Passing this lab is step one of the district’s safety program. Before you operate anything, your teacher still gives you hands-on demonstrations and a guided-practice sign-off on each piece of equipment - and nothing in this shop is ever operated without the instructor’s permission .
Permission & attention
The rule the district prints in capital letters: DO NOT OPERATE EQUIPMENT WITHOUT PERMISSION FROM THE INSTRUCTOR. Not before class, not during, not after - safety instruction and the instructor’s go-ahead come first, every time.
Keep your mind on the work. A moment of lost attention is how serious accidents happen.
No earbuds or headphones in the work environment - they mask warnings, callouts, and the sound of a machine going wrong. (Production intercom during shows is the one exception, used with discipline.)
When in doubt, ask the instructor - not the student next to you.
Dress for the shop
Shop safety starts before you touch a tool - with what you’re wearing:
Closed-toe shoes, every shop day. No sandals, no slides, no exceptions - dropped lumber doesn’t care how careful you were.
Long hair tied back. Hair near a spinning tool gets pulled in faster than you can react.
No dangling anything - jewelry, hoodie strings, loose sleeves, lanyards. If it hangs, it catches.
Sleeves rolled above the elbows , nothing loose at the wrists.
Gloves only where the task calls for them - rough lumber, hot fixtures, chemicals. Never around spinning blades or bits: a caught glove pulls the hand in with it.
No running, no horseplay. Ever. The shop is the one room where a joke shove can cost a finger.
Know your hazards
A theatre shop is full of things that can hurt you if you don’t see them coming: sharp tools and blades , things falling from above , dust in the air , loud noise , and cords, lumber, and clutter you can trip over .
Your first safety skill is simple: look around and name the hazards before you start any task. If you can’t name what could go wrong, you’re not ready to start.
Spot the hazards
Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Lifting & carrying
More shop injuries come from carrying than from cutting:
Lift with your legs - squat, keep your back near-vertical, hug the load close, stand. Your back is not a crane.
Never lift more than you can handle easily - over about 25 pounds, get help.
Clear your path before you pick anything up - most carrying accidents are collisions with things left on the floor or hanging at head height.
Team-lift anything long or heavy , and lift on a call: “ready - lift on three.” Same for setting down.
Carrying long stock: watch both ends , keep the front end high, and call the corners (“coming around!”).
Gloves for rough lumber - splinters are the tax on bare hands.
Watch the pinch points when setting anything down: fingers out from under, always.
Emergencies & injuries
Know these before you touch a single tool:
If anyone yells “STOP” or “HOLD” , all work stops instantly - no questions, hands off, tools down.
Every injury gets reported to the teacher immediately - no matter how slight - and an incident report is filed. A tiny cut in a dusty shop gets infected; a “small” incident often means a hazard that will hurt the next person worse.
Know where the first-aid kit lives.
Fire gets its own full module - alarms, exits, extinguisher classes, and how to report one.
PPE without reminders
You’ve been introduced to PPE - now the bar is higher: select and wear the correct PPE for the task without being reminded .
Safety glasses for cutting and drilling, hearing protection around loud tools, dust protection when sanding. Nobody should ever have to tell you. If you’re reaching for a tool, you’ve already reached for your PPE.
Pre-use check: good to go, or report it?
Before using any tool you do a pre-use safety check - and anything unsafe gets reported , even if it isn’t yours. Sort each finding:
Dust - the slow hazard
The hazard you can’t feel hurting you:
Fine wood dust harms lungs over years , not minutes - which is why nobody takes it seriously until it’s late. Take it seriously now.
Dust collection on whenever the sander or saws run.
Clean up dust by sweeping or vacuuming - never by blasting it airborne with the compressor.
The dust mask is for making dust and for cleaning it up .
The air hose is not a broom
You’re covered in sawdust after sanding, and the compressor hose is right there. Blow yourself off?
Chemicals, SDS & the eyewash station
Paint, adhesives, solvents, and fog fluid are chemicals - and every chemical in the shop has a Safety Data Sheet (SDS) :
The SDS binder lists each product’s hazards, handling rules, and first aid. Know where it lives.
Chemicals stay in labeled, closed containers - never in mystery cups or water bottles.
Rubber gloves are the exception to the no-gloves rule: wear them for stains, resins, and bleaches (never around spinning machines).
Know where the eyewash station is before you need it - you won’t be able to look for it with chemicals in your eyes.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 102
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
102
ASK THE ROOM
Spot the hazards
Shop Safety & PPE
Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Which items are hazards?
• Extension cord run across the walkway
• Hand saw left blade-up on the bench
• Boxes stacked in front of the exit
• Open drink next to the work area
• Board with a nail sticking out
• Safety glasses on the PPE shelf
• Fire extinguisher on its wall hook
• Swept floor, broom racked
Notes: Ask students to commit before advancing.
Prompt: Time to use that skill. Look around this shop and tap everything that’s a hazard - there are 5 .
Extension cord run across the walkway: Trip hazard - cords get routed out of walking paths.
Hand saw left blade-up on the bench: Sharp edges get sheathed or racked, never left out.
Boxes stacked in front of the exit: Exits stay clear - always.
Open drink next to the work area: Spills around tools and electricity - drinks stay out of the shop.
Board with a nail sticking out: Pull or bend nails the moment you see them.
Safety glasses on the PPE shelf: that’s exactly where PPE belongs.
Fire extinguisher on its wall hook: visible and ready - just right.
Swept floor, broom racked: good housekeeping is what prevents hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 103
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
103
REVEAL
Spot the hazards
Shop Safety & PPE
HAZARDS
• Extension cord run across the walkway
• Hand saw left blade-up on the bench
• Boxes stacked in front of the exit
• Open drink next to the work area
• Board with a nail sticking out
SAFE / CORRECT
• Safety glasses on the PPE shelf
• Fire extinguisher on its wall hook
• Swept floor, broom racked
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Extension cord run across the walkway: Trip hazard - cords get routed out of walking paths.
Hand saw left blade-up on the bench: Sharp edges get sheathed or racked, never left out.
Boxes stacked in front of the exit: Exits stay clear - always.
Open drink next to the work area: Spills around tools and electricity - drinks stay out of the shop.
Board with a nail sticking out: Pull or bend nails the moment you see them.
Safety glasses on the PPE shelf: that’s exactly where PPE belongs.
Fire extinguisher on its wall hook: visible and ready - just right.
Swept floor, broom racked: good housekeeping is what prevents hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 104
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 02 OF 10
104
MODULE 02
Fire Safety & Emergencies
Alarms, exits, extinguisher classes, reporting a fire, and flammable storage.
Alarms, drills & exits: Fire safety starts before there’s ever a fire: Know the fire bell/alarm and the fire-drill procedure for the shop and the theatre.
Reporting a fire: If you discover a fire: Immediately notify the closest adult with the exact location and the nature of the fire (what’s burning).
Fire classes & extinguishers: Extinguishers match the fire - the wrong one can make it worse: Class A - wood, paper, cloth.
Flammables, rags & finishes: The scene shop makes its own fire hazards: Rags soaked with finish, stain, or solvent go in a covered metal container - oily rags in a pile can…
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Alarms, drills & exits
Fire safety starts before there’s ever a fire:
Know the fire bell/alarm and the fire-drill procedure for the shop and the theatre.
Know every fire-exit location - and keep all exits and corridors clear at all times . In an evacuation, a blocked hallway costs lives, not minutes.
Know the types and locations of the fire extinguishers in your space - before you need them.
Reporting a fire
If you discover a fire:
Immediately notify the closest adult with the exact location and the nature of the fire (what’s burning).
Do NOT shout “Fire!” - panic in a crowded theatre is its own disaster; information moves faster than fear.
If someone’s clothing catches fire: smother the flames - get them down and roll them in a blanket if one is close.
Fire classes & extinguishers
Extinguishers match the fire - the wrong one can make it worse:
Class A - wood, paper, cloth. Water or CO₂ works.
Class B - flammable liquids (paint thinner, solvents). Smother it : foam or CO₂. Water spreads it.
Class C - electrical equipment. Non-conducting only : CO₂ or dry powder. Never water - electricity travels up the stream to you.
Pick the extinguisher
Match the fire to the response:
You spot smoke
You smell smoke and find a small fire behind the scene shop. What do you do first?
Flammables, rags & finishes
The scene shop makes its own fire hazards:
Rags soaked with finish, stain, or solvent go in a covered metal container - oily rags in a pile can self-ignite . That’s not a myth; it’s chemistry.
Use finishes and solvents only in well-ventilated areas, away from open flame and heat.
Keep flammable items away from lighting instruments - and instruments away from soft goods, paper, and scenery that could cook against a hot fixture.
Pyrotechnics, flame effects, and prop firearms are never student-operated - district approval and the fire marshal come first, every time.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 105
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
105
ASK THE ROOM
Pick the extinguisher
Fire Safety & Emergencies
Match the fire to the response:
Sort each item into: Water works (Class A) / CO₂ / dry powder only
• Scrap lumber and paper burning in the bin
• A dimmer rack sparking and smoking
• Spilled paint thinner catches fire
• Muslin scraps smoldering in the paint corner
Notes: Ask students to commit before advancing.
Prompt: Match the fire to the response:
Scrap lumber and paper burning in the bin: Class A - ordinary combustibles; water or CO₂.
A dimmer rack sparking and smoking: Class C electrical - non-conducting extinguisher, never water.
Spilled paint thinner catches fire: Class B flammable liquid - smother with foam or CO₂; water spreads it.
Muslin scraps smoldering in the paint corner: Class A - cloth burns like paper.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 106
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
106
REVEAL
Pick the extinguisher
Fire Safety & Emergencies
Water works (Class A)
• Scrap lumber and paper burning in the bin
• Muslin scraps smoldering in the paint corner
CO₂ / dry powder only
• A dimmer rack sparking and smoking
• Spilled paint thinner catches fire
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Scrap lumber and paper burning in the bin: Class A - ordinary combustibles; water or CO₂.
A dimmer rack sparking and smoking: Class C electrical - non-conducting extinguisher, never water.
Spilled paint thinner catches fire: Class B flammable liquid - smother with foam or CO₂; water spreads it.
Muslin scraps smoldering in the paint corner: Class A - cloth burns like paper.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 107
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 03 OF 10
107
MODULE 03
Your Tools This Year
What’s new for you this year - and everything you carry forward.
Grade 8 - Stagecraft: This is the year power tools begin.
2 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Grade 8 - Stagecraft
This is the year power tools begin.
Hand tools - hammer, tape measure, speed/framing square, utility knife, hand saw, screwdrivers.
Power & pneumatic (safety orientation required, supervised) - jigsaw, compound miter saw, panel saw, impact driver, random orbital sander, narrow crown stapler, framing nailer.
Painting - brushes & rollers.
Every power and pneumatic tool requires passing its safety orientation first .
Cleared for you - or not yet?
Which of these are you cleared to use at your grade level (after passing each tool’s safety orientation)?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 108
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
108
ASK THE ROOM
Cleared for you - or not yet?
Your Tools This Year
Which of these are you cleared to use at your grade level (after passing each tool’s safety orientation)?
Sort each item into: Cleared for me / Not yet
• Compound miter saw
• Random orbital sander
• Framing nailer
• Table saw
• Band saw
• Palm router
Notes: Ask students to commit before advancing.
Prompt: Which of these are you cleared to use at your grade level (after passing each tool’s safety orientation)?
Compound miter saw: Yours after its safety orientation, with supervision.
Random orbital sander: Yours after its safety orientation, with supervision.
Framing nailer: Pneumatic tools are in - after the orientation.
Table saw: Stationary machines start in Grade 10.
Band saw: Stationary machines start in Grade 10.
Palm router: Stationary machines start in Grade 10.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 109
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
109
REVEAL
Cleared for you - or not yet?
Your Tools This Year
Cleared for me
• Compound miter saw
• Random orbital sander
• Framing nailer
Not yet
• Table saw
• Band saw
• Palm router
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Compound miter saw: Yours after its safety orientation, with supervision.
Random orbital sander: Yours after its safety orientation, with supervision.
Framing nailer: Pneumatic tools are in - after the orientation.
Table saw: Stationary machines start in Grade 10.
Band saw: Stationary machines start in Grade 10.
Palm router: Stationary machines start in Grade 10.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 110
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 04 OF 10
110
MODULE 04
Hand Tools & Knives
Tape measure, utility knife, squares, hammer, screwdrivers, hand saw - the tools everything else is built on.
Measuring & layout tools: Even “safe” tools have rules: Tape measure - control the blade on the way back in; a spring-loaded steel edge returning at full speed can cut.
Utility knife: The tool you’ll use most, and the one that sends the most people to the first-aid kit: • A sharp blade is safer than a dull one - it needs less force, so…
Hammer, screwdrivers & hand saw: Hammer - check the head is tight before swinging; clear your swing arc (people and your other hand); start nails with a light tap, fingers gone before…
Squares & layout at the bench: Layout tools earn their keep in Stagecraft: Speed square - your crosscut guide: hold it firm with your thumb up on its face, and run the saw along the…
7 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Measuring & layout tools
Even “safe” tools have rules:
Tape measure - control the blade on the way back in; a spring-loaded steel edge returning at full speed can cut. Watch the hook edge on long pulls.
Marking & layout tools - carry pointed tools (awls, compasses, pencils) tip-down , and never walk with them in a pocket point-up.
Every tool goes back to its rack when you set it down - a bench you can’t see the surface of is a bench hiding a blade.
Utility knife
The tool you’ll use most, and the one that sends the most people to the first-aid kit:
• A sharp blade is safer than a dull one - it needs less force, so it slips less. Swap dull blades.
• Cut away from your body - and away from the hand bracing the work. Ask: “if this slips, where does the blade finish?”
• Cut on a mat or scrap , never on the bare table or your knee.
• Retract the blade the second you stop cutting. No exceptions.
• Pass it handle-first , blade retracted. Used snap-off blades go in the taped sharps container, never loose in the trash.
Change a utility-knife blade - in order
Put a safe blade change in order. Tap the first step, then the next…
Hammer, screwdrivers & hand saw
Hammer - check the head is tight before swinging; clear your swing arc (people and your other hand); start nails with a light tap, fingers gone before the real swing.
Screwdrivers - use the right size tip so it doesn’t cam out; never drive toward your palm or hold the work in your hand; a screwdriver is not a chisel or a pry bar - tips snap and hands slip.
Hand saw - start the kerf with short, light strokes; keep your free hand clear of the cut line; support the off-cut so it doesn’t tear free at the end.
Squares & layout at the bench
Layout tools earn their keep in Stagecraft:
Speed square - your crosscut guide: hold it firm with your thumb up on its face, and run the saw along the edge. Fingers stay on top of the square, never on the blade side.
Framing square - for sheet layout and checking corners; two people hold it for long lines.
Mark the waste side of every line with an X - half the “wrong cuts” in a shop are right cuts on the wrong side.
A sharp pencil line beats a fat one; for fine work, a knife line beats both (utility-knife rules apply).
Hand-tool habits
Sort each habit:
Make a hand-saw cut - in order
Put a clean, safe hand-saw cut in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 111
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
111
ASK THE ROOM
Change a utility-knife blade - in order
Hand Tools & Knives
Put a safe blade change in order. Tap the first step, then the next…
Put the steps in the safest order.
• Test the slider and lock before cutting
• Seat the new blade and close the knife
• Old blade goes into the taped sharps container
• Open the knife and lift out the old blade
• Retract the blade fully
Notes: Ask students to commit before advancing.
Prompt: Put a safe blade change in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 112
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
112
REVEAL
Change a utility-knife blade - in order
Hand Tools & Knives
CORRECT ORDER
• 1. Retract the blade fully
• 2. Open the knife and lift out the old blade
• 3. Old blade goes into the taped sharps container
• 4. Seat the new blade and close the knife
• 5. Test the slider and lock before cutting
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 113
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 05 OF 10
113
MODULE 05
Costume & Craft Tools
Needles, pins, shears, papier-mâché & armatures, the sewing machine, and the hot-wire foam knife.
Needles, pins & hand sewing: Small tools, real rules: Count your needles and pins out - and back in.
Scissors & pattern tools: Fabric shears are seriously sharp - that’s the point.
Papier-mâché & armatures: Props building has its own sharp ends: Cut armature wire with wire cutters, never scissors - scissors get ruined, and ruined tools slip.
4 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Needles, pins & hand sewing
Small tools, real rules:
Count your needles and pins out - and back in. A lost pin ends up in a costume, a couch, or a foot.
Pins live in a pincushion or magnetic tray - never in your lips, never in your clothes.
Broken needles and bent pins get taped and binned , not tossed loose.
Anything sharp gets passed handle-first .
Scissors & pattern tools
Fabric shears are seriously sharp - that’s the point.
• Carry them closed, point-down . Never run - it’s a cliché because it’s true.
• Pass them handle-first .
• Cut on the table , fabric flat, free hand behind the blades - not in the air toward yourself.
• Fabric shears cut fabric only : paper and cardboard dull them into tools that slip.
Papier-mâché & armatures
Props building has its own sharp ends:
Cut armature wire with wire cutters, never scissors - scissors get ruined, and ruined tools slip.
Every cut wire end gets bent back or taped immediately. Armature wires stick out at exactly eye height on a crowded work table.
Paste makes floors slick - wipe drips when they happen, not at cleanup.
Cover cuts on your hands before pasting, and wash up after - paste and sealers aren’t hand lotion.
Wire ends
You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 114
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
114
ASK THE ROOM
Wire ends
Costume & Craft Tools
You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Choose the safest response.
• A. Finish the layer first, then deal with it
• B. Bend it back or tape it immediately
• C. Point it out to the people nearby
• D. Move your own face away from it
Notes: Ask students to commit before advancing.
Prompt: You just clipped an armature wire and the cut end sticks out at face height over the work table. What happens right now?
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 115
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
115
REVEAL
Wire ends
Costume & Craft Tools
CORRECT ANSWER
• Bend it back or tape it immediately
WHY IT MATTERS
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Wire ends at eye height don’t wait for cleanup time - they get bent back or capped the moment they exist.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 116
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 06 OF 10
116
MODULE 06
Power Tool Basics
The rules that cover every power and pneumatic tool, and your path to qualification.
Rules that never change: For every power and pneumatic tool, at every grade level: • Guards stay on and working.
Your path: orientation → supervision → independence: Qualification is a ladder, and every tool has its own rung: 1⃣ Safety orientation (Grade 8) - you pass an orientation for each tool, then perform…
Cords, hoses & your workspace: The cable end of tool safety: The cord or hose stays behind the tool, never in the cut path - check before every cut, not after.
Clamp it, support it: Most “tool accidents” are really workholding accidents : A clamp beats your strongest grip - and it never flinches.
Pneumatic power: the air rules: The stapler and nailer run on compressed air, which adds rules of their own: • Treat every air tool as loaded.
8 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Rules that never change
For every power and pneumatic tool, at every grade level:
• Guards stay on and working. A tool with a faulty guard doesn’t get used - it gets reported.
• PPE first - safety glasses always; hearing and dust protection as the task demands.
• Correct body position - balanced stance, hands clear of the cut line, never reaching across a blade.
• Disconnect power or air before adjusting - blade changes, depth settings, or clearing jams happen only on a dead tool.
Your path: orientation → supervision → independence
Qualification is a ladder, and every tool has its own rung:
1⃣ Safety orientation (Grade 8) - you pass an orientation for each tool, then perform fundamental operations under direct supervision : straight cuts, crosscuts, driving fasteners, sanding flat stock.
2⃣ General supervision (Grade 9) - you set up and operate each tool with the teacher in the shop, not at your elbow, producing accurate cuts and secure assemblies.
3⃣ Independent qualification (Grade 10+) - you pass an independent-use qualification per tool, handle routine adjustments yourself, and help train peers.
Grade level alone never qualifies you - passing the orientation or qualification for that specific tool does .
Cords, hoses & your workspace
The cable end of tool safety:
The cord or hose stays behind the tool, never in the cut path - check before every cut, not after.
Never carry a tool by its cord , and unplug by gripping the plug , not yanking the cable.
Disconnecting an air hose: shut off the air and bleed the pressure first , and keep hold of the coupling - a charged hose whips.
Cords and hoses route along walls and out of walkways , same as the shop rule you already know.
Clamp it, support it
Most “tool accidents” are really workholding accidents :
A clamp beats your strongest grip - and it never flinches.
Long stock gets outfeed support - a sawhorse, a stand, or a partner on a callout.
The cut line hangs clear of the bench - cutting into the table pinches the blade and ruins both.
Never cut work resting on your knee or held in the air.
Know what’s under and behind the cut before you start it.
Set up a cut - in order
Put the steps of a safe power-tool cut in order. Tap the first step, then the next…
Pneumatic power: the air rules
The stapler and nailer run on compressed air, which adds rules of their own:
• Treat every air tool as loaded. Finger off the trigger until the nose is on the work.
• Never point one at anyone - including yourself. Ever. Even “empty.”
• Disconnect the air line before clearing a jam, adjusting, or handing it over.
• Use the tool’s correct air pressure - too high blows fasteners through the work; too low jams and double-fires.
• Hoses get routed out of walkways , like every cord.
Jammed nailer
The framing nailer jams mid-wall. Before you touch the jam, you…
Cord in the lane
Mid-setup, you notice the jigsaw’s own cord crossing under the line you’re about to cut. You…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 117
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
117
ASK THE ROOM
Set up a cut - in order
Power Tool Basics
Put the steps of a safe power-tool cut in order. Tap the first step, then the next…
Put the steps in the safest order.
• Let the blade stop completely before reaching in
• Make the cut with correct body position
• Clear the work area and support your stock
• Check guards, blade, and cord or hose
• Put on your PPE
Notes: Ask students to commit before advancing.
Prompt: Put the steps of a safe power-tool cut in order. Tap the first step, then the next…
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 118
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · CLASSROOM CHECK
118
REVEAL
Set up a cut - in order
Power Tool Basics
CORRECT ORDER
• 1. Put on your PPE
• 2. Check guards, blade, and cord or hose
• 3. Clear the work area and support your stock
• 4. Make the cut with correct body position
• 5. Let the blade stop completely before reaching in
Notes: Reveal the answer and ask one student to explain the rule in their own words.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 119
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 07 OF 10
119
MODULE 07
Power Saws: Jigsaw, Miter, Panel
Tool-by-tool specifics for the three saws you qualified on in Stagecraft.
Jigsaw: The curve-cutter.
Jigsaw - blades, curves & cutouts: Getting the cut you want, safely: Match the blade to the material - wood, metal, and scroll blades are different animals; the wrong one burns, wanders,…
Miter saw - angles & short stock: The setups that catch people: Set and lock the angle , then test on scrap - an unlocked table creeps mid-cut.
Panel saw: The sheet-goods saw.
Rip vs crosscut - know your cut: Two words you’ll hear every day in the shop: A crosscut goes across the grain - cutting a 2×4 to length.
11 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Jigsaw
The curve-cutter. Its specifics:
• Clamp your stock - small pieces walk with the blade and take fingers along.
• Base plate flat on the work before you pull the trigger.
• Know what’s under the cut - the blade sticks out below the stock. Nothing under the line: not the bench edge, not the cord, not your hand.
• Let the blade stop before lifting the saw out of the cut.
• Forcing the cut bends and snaps blades - let the blade do the work . Unplug to change blades.
Jigsaw - blades, curves & cutouts
Getting the cut you want, safely:
Match the blade to the material - wood, metal, and scroll blades are different animals; the wrong one burns, wanders, and snaps.
Tight curves want narrow blades - and really tight curves want relief cuts first, so the blade never binds.
Interior cutouts start from a drilled starter hole , never from tipping the saw into the surface.
A blade that starts wandering off your line is worn out - swap it (unplugged) instead of steering harder.
Compound miter saw
The crosscut machine. Its specifics:
• Stock tight against the fence - always. A gap lets the blade grab and slam the stock.
• Hands outside the no-hand zone (at least 6 inches from the blade path). Never cross your arms - left hand holding the right side of the blade is how people meet the blade.
• Full speed before the cut - let it spin up, then bring it down smoothly.
• After the cut, keep the blade down until it stops - a spinning blade coming up can grab the off-cut and throw it.
• Support long stock on both ends; never balance it.
Miter saw - angles & short stock
The setups that catch people:
Set and lock the angle , then test on scrap - an unlocked table creeps mid-cut.
Long stock gets a stand or a partner (on a callout) at the far end - a see-sawing board pinches the blade.
Anything too short to hold outside the no-hand zone gets clamped - or cut from a longer board so your hand never gets close.
If a cut would put your fingers inside the zone, that cut doesn’t happen that way. There is always another way.
Miter saw check
You just finished a cut on the miter saw. When do you raise the blade?
The short piece
You need a 3-inch block. Holding it for the miter cut would put your fingers inside the no-hand zone. You…
Panel saw
The sheet-goods saw. Its specifics:
• Seat the sheet fully on the rollers/rails before cutting - a cocked sheet binds the blade.
• Both hands on the carriage handle. Never steady the sheet with a hand near the cut line.
• Let the carriage return home before touching anything.
• Mind the off-cut - full sheets are heavy, and freed panels pinch fingers and toes. Get help catching big pieces.
Panel saw sheet cut - in order
Put a full-sheet cut on the panel saw in order. Tap the first step, then the next…
Rip vs crosscut - know your cut
Two words you’ll hear every day in the shop:
A crosscut goes across the grain - cutting a 2×4 to length. That’s the miter saw’s job.
A rip cut runs along the grain or the length of a sheet. At your grade, sheet rips happen on the panel saw .
The table saw - the shop’s main rip machine - waits for Grade 10 and its own orientation.
Naming the cut tells you the tool; the tool tells you the rules.
Which saw for the job?
Choosing the right saw is a safety skill - the wrong tool fights you. Match each cut to its saw:
Spot what’s wrong: the cutting station
Walk the saw stations and tap the 4 problems .
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 120
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 08 OF 10
120
MODULE 08
Drivers, Sanders & Nailers
Impact driver, random orbital sander, narrow crown stapler, and framing nailer.
Impact driver: Small tool, huge torque.
Bits & torque: The details that separate clean driving from stripped screws: Right bit, right size - a PH2 in a PH3 screw strips both.
Random orbital sander: The dust machine.
Grits & technique: Sanding well is sanding safely - fighting the tool is what causes slips: Work the grit ladder: 80 → 120 → 220 .
Stapler & framing nailer: You learned the air rules in Power Tool Basics - here are the gun-specific ones: • The contact safety tip on the nose is what stops accidental fires.
7 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Impact driver
Small tool, huge torque. Its specifics:
• Seat the bit fully in the screw head before pulling the trigger - a half-seated bit cams out and skates.
• Hand off the fastener line. When the bit slips, it goes exactly where your hand was going to be.
• Start slow to set the threads, then run it home.
• Brace small work - the driver will happily spin the workpiece instead of the screw.
• Eye protection: screw heads snap and bits shatter.
Bits & torque
The details that separate clean driving from stripped screws:
Right bit, right size - a PH2 in a PH3 screw strips both. Check before you drive.
Worn bits get binned , not babied - a rounded bit cams out no matter how hard you push.
Impact drivers hammer - that rattle is the mechanism working, and it’s loud : hearing protection when the driving runs long.
Small screws snap under full impact - ease off as the head seats.
Pilot holes near edges stop the split before it starts.
Random orbital sander
The dust machine. Its specifics:
• Dust protection on, dust collection attached - fine dust is the hazard you can’t see hurting you.
• Don’t press. The tool’s weight is enough; leaning on it burns the paper, scorches the stock, and stalls the pad.
• Let the pad stop before you set it down - a live sander walks off the bench.
• Secure small pieces ; the sander is strong enough to launch them.
• Keep the cord behind the tool , never under the pad.
Grits & technique
Sanding well is sanding safely - fighting the tool is what causes slips:
Work the grit ladder: 80 → 120 → 220 . Skipping grits means pressing harder for less result.
Keep the pad flat and moving - parking it in one spot digs a dish you’ll sand an hour to fix.
Edges round over in seconds - ease up when you get near them.
Let the paper do the work: if you’re pressing, the paper’s done - change it .
Stapler & framing nailer
You learned the air rules in Power Tool Basics - here are the gun-specific ones:
• The contact safety tip on the nose is what stops accidental fires. It is never held down, taped, or bypassed . Never.
• Sequential fire : nose on the work first, then the trigger.
• Hands at least a hand-span from the fire line. Staples and nails follow the grain and deflect off knots - they can exit the wood sideways .
• The framing nailer recoils - grip it, expect it.
• Carry with your finger off the trigger ; disconnect air to clear jams or hand it off.
Nailer check
Your palm is bracing a stud about 2 inches from where you’re about to shoot a nail. Fire?
Driver & sander habits
Sort each habit:
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 121
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 09 OF 10
121
MODULE 09
Lighting & Electrics
Ladders, fixture hardware, gels & gobos, cable care, hot focus, and electrical hazards.
Ladders & working at height: Know the ladder and working-at-height rules and be able to state them: • A ladder is set on stable ground and steadied - never climbed alone in the shop.
Power, plugs & equipment care: The rules for anything with a plug - consoles, playback, monitors, practicals: Dry hands only on switches, plugs, and equipment - and never use…
Cable care & over-under: Cable is equipment, not rope: Coil over-under so it pays out flat without kinks - a kinked cable is a damaged cable waiting to happen.
Inspect before you use: You now work safely at height and around circuits with general supervision .
Hot focus: Refocusing fixtures that have been running is normal electrics work - done the right way: Gloves for a hot fixture - or kill the channel and let it cool.
9 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Ladders & working at height
Know the ladder and working-at-height rules and be able to state them:
• A ladder is set on stable ground and steadied - never climbed alone in the shop.
• Keep three points of contact and never overreach; climb down and move the ladder instead.
• Nothing is carried up that can’t be carried safely; nothing gets dropped, ever.
Anyone working below wears the hazard in mind: if work is happening overhead, stay clear or call it out.
The hardware: C-clamp, wrench & safety cable
Your first lighting tools are hardware - and hardware has rules:
The wrench fits the bolt snugly - an adjustable wrench gets set tight; a loose fit rounds the bolt and skins knuckles.
Tighten the C-clamp snug, not gorilla-tight - over-torquing cracks clamps and pipes.
At height, the wrench is tethered or in a closed pocket - a dropped wrench from the grid is a missile with your name on the incident report.
The safety cable goes through the fixture’s yoke and around the pipe , clipped back on itself - so it catches the fixture even if the whole clamp lets go.
Power, plugs & equipment care
The rules for anything with a plug - consoles, playback, monitors, practicals:
Dry hands only on switches, plugs, and equipment - and never use electrical equipment near water or wet floors. Moisture conducts.
Before moving any equipment, disconnect and clear its cables. A dangling cord is a trip line and a broken connector.
Never defeat grounding - no forcing a three-prong plug into a two-prong outlet, ever. That third pin is what keeps a fault from going through you.
Connect gear only to the power type marked on it ; route cords where they can’t be walked on or pinched .
Give equipment ventilation - racks and amps cook when boxed in - and keep liquids and stray objects out of the openings.
Don’t service beyond the manual. Anything deeper goes to qualified personnel.
Gels, gobos & hot fronts
Handling the pretty parts safely:
Gels ride in gel frames - a loose gel stuffed in a fixture melts, smokes, and stinks up a performance.
Gobos are thin sharp steel - handle by the rim, like a razor-edged coin.
Warn everyone before switching an instrument on - nobody should be staring into a light that doesn’t announce itself.
Assume any instrument is extremely hot - even switched off. The front end (barrel, gel frame, shutters) holds burn heat long after the cue.
Keep instruments and flammable items apart - soft goods, paper, and scenery cook against a hot fixture.
Ask before touching any hung fixture - you don’t know how long it’s been running.
Cable care & over-under
Cable is equipment, not rope:
Coil over-under so it pays out flat without kinks - a kinked cable is a damaged cable waiting to happen.
Out of walkways , always - tape it down or reroute it.
Never yank a connector out by its cable - grip the connector itself.
Never pinch cable in doorways or run it over sharp edges .
Wet floors and cable don’t mix - dry first, then run power.
Hang a fixture - in order
Put the steps of hanging a fixture in order. Tap the first step, then the next…
Inspect before you use
You now work safely at height and around circuits with general supervision . That comes with a duty: inspect cables and fixtures before use - cracked connectors, frayed jacket, loose clamp, missing safety cable.
And when you find a fault, report it without prompting . A damaged cable that goes back in the bin unfixed is a trap for the next person.
Lock-out / tag-out
When equipment is unsafe, it comes out of service - visibly :
A tag (or lock) on a tool, cable, or machine means: dead until the instructor clears it . You don’t use it, you don’t “just test it,” and you never remove the tag.
That’s the student half of lock-out/tag-out - the industry system that keeps someone from powering up gear another person is working on.
The other half: your instructor inspects equipment weekly and documents it. Your pre-use inspection is the daily layer on top of that.
Hot focus
Refocusing fixtures that have been running is normal electrics work - done the right way:
Gloves for a hot fixture - or kill the channel and let it cool. A Source Four that’s been on all rehearsal blisters skin.
Loosen the right bolt - know your pan bolt from your tilt bolt so the unit moves where you expect instead of swinging free.
Wrench tethered or pocketed , same as every trip up the ladder.
Call your moves: “going into channel 12” - so the board op doesn’t light you up mid-grab.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 122
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · MODULE 10 OF 10
122
MODULE 10
Hearing & Audio Safety
Hearing conservation, SPL awareness, and safe speaker handling.
Protect your hearing: Sound level is measured as SPL (sound pressure level).
Headsets & comms: The “no earbuds in the shop” rule has a show-business nuance: Personal earbuds and headphones never belong in the work environment - they mask callouts,…
Fog, haze & atmospherics: Atmosphere looks like magic and behaves like a chemical plus a slip hazard: Use only approved fluids in fog and haze machines - the fluid’s SDS lives in…
Handling & rigging speakers: Speakers are heavy, awkward, and often end up over people’s heads.
6 grade-level sections
Notes: Teach the essential rules on this overview, then use the full source notes below as needed.
Protect your hearing
Sound level is measured as SPL (sound pressure level). Loud sound damages the tiny hair cells in your inner ear - and that damage is cumulative and permanent . It never heals, it only adds up.
So: wear hearing protection around loud tools and loud playback, keep your distance from speakers at show level, and treat ringing ears as a warning you already went too far.
Ringing ears
After a loud work session, your ears are ringing. What does that mean?
Headsets & comms
The “no earbuds in the shop” rule has a show-business nuance:
Personal earbuds and headphones never belong in the work environment - they mask callouts, warnings, and the sound of trouble.
Production intercom is the exception - it exists so the crew can hear each other . Keep one ear open around moving scenery, keep chatter short and clean, and never let a joke on comms bury a “heads up.”
If you can’t hear the room, you’re not safe in the room.
Fog, haze & atmospherics
Atmosphere looks like magic and behaves like a chemical plus a slip hazard:
Use only approved fluids in fog and haze machines - the fluid’s SDS lives in the binder like every other chemical.
Heavy fog is a respiratory consideration - ventilation matters, and anyone with asthma should say so before the effect runs.
Fluid residue makes decks slick - watch the floor near the machine and mop drips.
Fog and haze can trip smoke alarms - effects run only with the instructor, coordinated with the venue.
The machine’s output and nozzle get hot .
Handling & rigging speakers
Speakers are heavy, awkward, and often end up over people’s heads.
• Lift and move them with help - protect your back and the cabinet.
• Anything flown or mounted overhead uses rated hardware and rigging points , secured so it cannot fall.
• Never stack or perch a speaker where a bump or a cable snag could bring it down.
Speakers: do - or never?
Sort each speaker move:
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 123
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · TEST REVIEW
123
ASK THE ROOM
Certification test check
Shop Safety & PPE
A task is going to fill the air with fine dust. Which PPE does that call for?
Choose the safest response.
• A. Hearing protection
• B. Dust protection, like a dust mask
• C. Just safety glasses
• D. Gloves
Notes: Ask students to commit before advancing.
Prompt: A task is going to fill the air with fine dust. Which PPE does that call for?
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 124
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · TEST REVIEW
124
REVEAL
Certification test check
Shop Safety & PPE
CORRECT ANSWER
• Dust protection, like a dust mask
WHY IT MATTERS
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Dust protection is required whenever a task puts fine dust in the air; safety glasses and hearing protection guard against different hazards.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 125
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · TEST REVIEW
125
ASK THE ROOM
Certification test check
Fire Safety & Emergencies
You discover a fire in the scene shop. What do you do first?
Choose the safest response.
• A. Shout “Fire!” as loudly as possible
• B. Immediately notify the closest adult with the exact location and what’s burning
• C. Look for a bucket of water
• D. Open the doors for ventilation
Notes: Ask students to commit before advancing.
Prompt: You discover a fire in the scene shop. What do you do first?
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 126
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · TEST REVIEW
126
REVEAL
Certification test check
Fire Safety & Emergencies
CORRECT ANSWER
• Immediately notify the closest adult with the exact location and what’s burning
WHY IT MATTERS
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Exact location and the nature of the fire, to the nearest adult - and never a panic shout in a crowded space.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 127
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · TEST REVIEW
127
ASK THE ROOM
Certification test check
Your Tools This Year
Before using any power or pneumatic tool for the first time, you must…
Choose the safest response.
• A. Watch one other student use it
• B. Pass a safety orientation for that specific tool
• C. Just start on scrap wood
• D. Get permission from any older student
Notes: Ask students to commit before advancing.
Prompt: Before using any power or pneumatic tool for the first time, you must…
Every power and pneumatic tool requires passing its own safety orientation before you use it.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 128
SDSCPA
DESIGN & PRODUCTION · GRADE 8
SDSCPA · SAFETY LAB · GRADE 8 · TEST REVIEW
128
REVEAL
Certification test check
Your Tools This Year
CORRECT ANSWER
• Pass a safety orientation for that specific tool
WHY IT MATTERS
Every power and pneumatic tool requires passing its own safety orientation before you use it.
Notes: Reveal the answer and ask one student to explain the rule in their own words.
Every power and pneumatic tool requires passing its own safety orientation before you use it.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity

## Slide 129
SDSCPA
Certification is step one.
Safe equipment use still requires instructor permission, hands-on demonstrations, and guided-practice sign-off.
In the shop, “mostly safe” is not safe.
SDSCPA · SAFETY LAB · CERTIFICATION
129
Notes: Close by separating written certification from physical qualification. Students must still earn permission on each specific tool.
[Sources]
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/safety/index.html - SDSCPA-authored Safety Lab curriculum
- /Users/harrisonlange/Documents/GitHub/Scenic-Construction-App/SDSCPA_BRAND_GUIDE.md - SDSCPA visual identity